## Slide 1: Chapter 5. Image/Video Compression Standards
JPEG
H.261
MPEG-1
MPEG-2
H.263 & H.263+
MPEG-4
MPEG-7
MPEG-4 AVC/H.264
1

## Slide 2: JPEG

## Slide 3
JPEG : Background
JPEG = Joint Photographic Expert Group, Joint standards committee of ITU-T and ISO
Flexible standard for monochrome and color image compression
Intraframe coding scheme, optimized for still images
Flexible picture size
Coding of color components separately, arbitrary color spaces possible, best compression for Y/R-Y/B-Y
Variable compression ratio
Compression 24:1 for ITU-R 601 images without loss of quality visually
3

## Slide 4
JPEG
Mode of operations:
Sequential DCT
Progressive DCT
Sequential Lossless
Hierarchical
Sequential coding
Progressive coding
4

## Slide 5
JPEG : Goal
Allow applications to tradeoff easily between desired compression ratio and image quality
Work independently of image types
Have modest computational complexity that would allow software-only implementation even in low-end computers
Allow both sequential (single scan) and progressive (multiple scan) coding
Offers the option for hierarchical coding
Compress video frame by frame (MJPEG)
5

## Slide 6
Sequential DCT-based Systems
8x8 blocks
Compressed
image data
Compressed
image data
Source
image data
Reconstructed
image data
DCT
AC
DC
8x8 blocks
IDCT
DC
AC
6
Quantization
table
DPCM
Zigzag
scan
Entropy
encoder
Table
specification
DPCM
Quantization
table
Zigzag
scan
Entropy
decoder
Table
specification
Q
IQ
進行residue(DCt-DCt-1)
送差值

## Slide 7
Sequential DCT-based Systems
Baseline System: minimum capability that must be present in all JPEG systems (source sample precision limited to 8 bits; only Huffman coding for entropy coding; up to 2 sets of entropy coding tables)
Extended Sequential Systems: capabilities beyond the baseline requirement (source sample precision of 8 or 12 bits; can use Arithmetic coding; up to 4 sets of entropy coding tables)
7

## Slide 8
Original:
52 55 61 66 70 61 64 73
63 59 66 90 109 85 69 72
62 59 68 113 144 104 66 73
63 58 71 122 154 106 70 69
67 61 68 104 126 88 68 70
79 65 60 70 77 68 58 75
85 71 64 59 55 61 65 83
87 79 69 68 65 76 78 94
After level shift by -128:
- 76 - 73 - 67 - 62 - 58 - 67 - 64 - 55
- 65 - 69 - 62 - 38 - 19 - 43 - 59 - 56
- 66 - 69 - 60 - 15 16 - 24 - 62 - 55
- 65 - 70 - 57 - 6 26 - 22 - 58 - 59
- 61 - 67 - 60 - 24 - 2 - 40 - 60 - 58
- 49 - 63 - 68 - 58 - 51 - 65 - 70 - 53
- 43 - 57 - 64 - 69 - 73 - 67 - 63 - 45
- 41 - 49 - 59 - 60 - 63 - 52 - 50 - 34
An Example of JPEG Baseline System
8

## Slide 9
An Example of JPEG Baseline System
After DCT:
- 415 - 29 - 62 25 55 - 20 - 1 3
7 - 21 - 62 9 11 - 7 - 6 6
- 46 8 77 - 25 - 30 10 7 - 5
- 50 13 35 - 15 - 9 6 0 3
11 - 8 - 13 - 2 - 1 1 - 4 1
- 10 1 3 - 3 - 1 0 2 - 1
- 4 - 1 2 - 1 2 - 3 1 - 2
- 1 - 1 - 1 - 2 - 1 - 1 0 - 1
After quantization:
- 26 - 3 - 6 2 2 0 0 0
1 - 2 - 4 0 0 0 0 0
- 3 1 5 - 1 - 1 0 0 0
- 4 1 2 - 1 0 0 0 0
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
9

## Slide 10
Default Quantization Tables
Luminance Table:
Chrominance Table:
16 11 10 16 24 40 51 61
12 12 14 19 26 58 60 55
14 13 16 24 40 57 69 56
14 17 22 29 51 87 80 62
18 22 37 56 68 109 103 77
24 35 55 64 81 104 113 92
49 64 78 87 103 121 120 101
72 92 95 98 112 100 103 99
17 18 24 47 99 99 99 99
18 21 26 66 99 99 99 99
24 26 56 99 99 99 99 99
47 66 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99
10
數字為quantization step size，越左上角越重要，也就step要越小(細緻，保留資訊)

## Slide 11
Eye Sensitivity vs. Spatial Frequency
11
Y帶有訊息較多，CbCr相對少

## Slide 12
Resolution of Color Images
X
Y
X
Y
X
Y
X
Y
X/2
Y
X/2
Y
Same resolution
Different resolution
12

## Slide 13: Quantization of DCT Coefficients
13
(a),(c),(e) use the default quantization matrix
(b),(d),(f) use 4 times the default quantization matrix

## Slide 14
Zigzag scan
14

## Slide 15
After zigzag scan:
[ - 26 - 3 1 - 3 - 2 - 6 2 - 4 1 - 4 1 1 5
0 2 0 0 - 1 2 0 0 0 0 0 -1 -1 EOB]
After VLC:
1010110 0100 001 0100 0101 100001 0110 100011
001 100011 001 001 100101 11100110 110110
0110 11110100 000 1010
After DPCM of DC coefficient (assuming previous DC value of -17):
[ - 9 - 3 1 - 3 - 2 - 6 2 - 4 1 - 4 1 1 5
0 2 0 0 - 1 2 0 0 0 0 0 -1 -1 EOB]
An Example of JPEG Encoding
After RLC:
-9 (0,-3) (0,1) (0,-3) (0,-2) (0,-6) (0,2) (0,-4) (0,1) (0,-4) (0,1)
(0,1) (0,5) (1,2) (2,-1) (0,2) (5,-1) (0,-1) EOB
15

## Slide 16
Baseline DC Coefficient Coding
The difference DIFF is represented as a CAT.Value symbol
CAT: 0-11 (see the table on the next slide)
CAT=0: EOB (end of block)
Value is a fixed-length code with length indicated by the Category:
If Value > 0: positive binary number representation,
if Value < 0: one’s complement
Example:
DIFF=6: CAT=3 (100), Value=110  100110
DIFF=-3: CAT=2 (011), Value=00  01100
Blocki-1
Blocki
DCi
DCi-1
DIFF=DCi-DCi-1
16

## Slide 17
Baseline Coefficient Coding
DC
Category
(SSSS)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
AC
Category
(SSSS)
N/A
1
2
3
4
5
6
7
8
9
10
11
12
13
14
N/A
Coefficient
0
-1,1
-3,-2,2,3
-7,…,-4,4,…,7
-15,…,-8,8,…,15
-31,…,-16,16,…,31
-63,…,-32,32,…,63
-127,…,-64,64,…,127
-255,…,-128,128,…,255
-511,…,-256,256,…,511
-1023,…,-512,512,…,1023
-2047,…,-1024,1024,…,2047
-4095,…,-2048,2048,…,4095
-8191,…,-4096,4096,…,8191
-16383,…,-8192,8192,…,16383
-32767,…,-16384,16384,…,32767
17

## Slide 18
Default DC Codes (Luminance)
Category Huffman Code
0 00
1 010
2 011
3 100
4 101
5 110
6 1110
7 11110
8 111110
9 1111110
10 11111110
11 111111110
… ...
18

## Slide 19
Baseline AC Coefficient Coding
The zigzag sequence of DCT coefficients is represented as a sequence of (RRRRSSSS).Value symbols
RRRR: Zero-runlength
SSSS: Category
The maximum length of zero run is limited to 15
00000000:EOB (end of block)
RRRRSSSS is Huffman coded
Value is a fixed-length code with length indicated by the Category:
If Value > 0: positive binary number representation,
if Value < 0: one’s complement
19
11110000: zero-runlength=16 (15 zeros followed by a coefficient of zero amplitude)

## Slide 20
Decoder input:
1010110 0100 001 0100 0101 100001 0110 100011
001 100011 001 001 100101 11100110 110110
0110 11110100 000 1010
- 26 - 3 - 6 2 2 0 0 0
1 - 2 - 4 0 0 0 0 0
- 3 1 5 - 1 - 1 0 0 0
- 4 1 2 - 1 0 0 0 0
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
After RLD, Inverse DPCM, and Inverse zigzag scan:
An Example of JPEG Baseline System
After VLD:
-9 (0,-3) (0,1) (0,-3) (0,-2) (0,-6) (0,2) (0,-4) (0,1) (0,-4) (0,1)
(0,1) (0,5) (1,2) (2,-1) (0,2) (5,-1) (0,-1) EOB
20

## Slide 21
After inverse quantization:
- 416 - 33 - 60 32 48 0 0 0
12 - 24 - 56 0 0 0 0 0
- 42 13 80 - 24 - 40 0 0 0
- 56 17 44 - 29 0 0 0 0
18 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
After IDCT:
- 70 - 64 - 61 - 64 - 69 - 66 - 58 - 50
- 72 - 73 - 61 - 39 - 30 - 40 - 54 - 59
- 68 - 78 - 58 - 9 13 - 12 - 48 - 64
- 59 - 77 - 57 0 22 - 13 - 51 - 60
- 54 - 75 - 64 - 23 - 13 - 44 - 63 - 56
- 52 - 71 - 72 - 54 - 54 - 71 - 71 - 54
- 45 - 59 - 70 - 68 - 67 - 67 - 61 - 50
- 35 - 47 - 61 - 66 - 60 - 48 - 44 - 44
An Example of JPEG Baseline System
21

## Slide 22
An Example of JPEG Baseline System
After level shift by +128:
Error:
58 64 67 64 59 62 70 78
56 55 67 89 98 88 74 69
60 50 70 119 141 116 80 64
69 51 71 128 149 115 77 68
74 53 64 105 115 84 65 72
76 57 56 74 75 57 57 74
83 69 59 60 61 61 67 78
93 81 67 62 69 80 84 84
- 6 - 9 - 6 2 11 - 1 - 6 - 5
7 4 - 1 1 11 - 3 - 5 3
2 9 - 2 - 6 - 3 - 12 - 14 9
- 6 7 0 - 4 - 5 - 9 - 7 1
- 7 8 4 - 1 11 4 3 - 2
3 8 4 - 4 2 11 1 1
2 2 5 - 1 - 6 0 - 2 5
- 6 - 2 2 6 - 4 - 4 - 6 10
22

## Slide 23
Reconstruction in Sequential Mode
(a) 25% received
(b) 50% received
(c) 75% received
(d) 100% received
23

## Slide 24
Progressive DCT Mode
Successive approximation: the information is first sent
with lower precision and then refined in later scans
lower-frequency bands are (usually) sent first
Spectral selection: DCT coefficients are grouped into
"spectral" bands of related spatial frequencies and the
Require a coefficient memory buffer between quantizer
and the entropy encoder
Successive approximation gives better quality at low
bit-rates
24

## Slide 25
Reconstruction in Progressive Mode
25

## Slide 26
Progressive Coding with Spectral Selection and Successive Approximation
Image
Block reordering
FDCT
8
8
8x8
8x8
Sending
Sending
Coefficients zig-zag reordering and represented by 8 bits
1st scan
0
1st scan
Successive approximation
2nd scan
0
1
2
.
.
62
63
7 6 …. 1 0
MSB LSB
sending
Spectral selection
0
1
2
61
62
63
Nth scan
2nd scan
7 6 5 4 MSB
1
2
.
.
62
63
1
2
.
.
62
63
Sending
Sending
Sending
Sending
Sending
Sending
26

## Slide 27
Sequential Lossless Systems
Entropy
encoder
Lossless encoder
Compressed
Image Data
Table
specification
Source
Image Data
JPEG
Predictive
coder
Entropy
decoder
Lossless decoder
Compressed
Image Data
Table
specification
Reconstructed
Image Data
JPEG
Predictive
decoder
27

## Slide 28
Predictors for Lossless Coding
A
C
B
X
Selection-
value
Prediction
no prediction
A
B
C
A + B - C
A + ( B - C ) / 2
B + ( A - C ) / 2
( A + B ) / 2
0
1
2
3
4
5
6
7
* JPEG lossless coding typically produce ~2:1 compression
28

## Slide 29
Hierarchical Mode
The first stage (lowest resolution) is coded using one of the sequential or progressive JPEG modes
The output of each hierarchical stage is then upsampled and becomes the prediction for the next stage
29

## Slide 30
Hierarchical Multiresolution Encoding
30

## Slide 31
A Three-level Hierarchical Coder
Encoder
Decoder
4
Encoder
Decoder
2
2
Encoder
Decoder
2
Decoder
Decoder
Decoder
2
2
4
X
X'
Xj’
Xi’
X4’
X2’
S
1
S
2
S
3
X4
X2
31
Encoder

## Slide 32
JPEG Performance
Bits/pixel
>= 2
1.5
0.75
0.5
0.25
Quality
Indistinguishable
Excellent
Very Good
Good
Fair
Compression Ratio
8-to-1
10.7-to-1
21.4-to-1
32-to-1
64-to-1
32

## Slide 33
Example of Artifacts due to JPEG Coding
Original
JPEG Encoded
33

## Slide 34
Subjective Quality of JPEG
Original Lena Image
File Size = 256K bytes
Compressed Lena Image
File Size = 13K bytes
34

## Slide 35: H.261
35

## Slide 36
H.261 Video Coding Standard
Rec. H.261, "Video Codec for Audiovisual Services at
px64 kb/s," (p=1,2,...,30) completed and approved in
December 1990
Intended applications: videotelephony (p = 1 or 2) and
videoconferencing (p  6)
Capable of real-time operation with minimum delay
Offer a factor of about three in compression compared
to JPEG by using interframe coding to remove the
temporal redundancy
36

## Slide 37
H.261 Video Source Formats
* The numbers in the parentheses represent active pixels
CIF (Common Intermediate Format) is optional and QCIF (Quarter CIF)
Uncompressed bit-rate for transmitting CIF and QCIF
at 30 fps are 36.5 Mb/s and 9.12 Mb/s, respectively
QCIF
CIF
Format
Lines/
Frame
288
144
144
Pixels/
Line
360 (352)
180 (176)
180 (176)
Lines/
Frame
144
72
72
Pixels/
Line
180 (176)
90 (88)
90 (88)
37
Signal
Component
Luminance
(Y)
Chrominance
()
Chrominance
()
* 4:2:0 Y
is mandatory

## Slide 38
Arrangement of Blocks in A Picture
CIF
QCIF
GOB (Group Of
Blocks) in a picture
Macroblocks in a GOB
Blocks in a macroblock
1
2
3
4
5
6
7
8
9
10
11
12
1
2
3
1
2
3
4
5
6
Y
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
1
2
38

## Slide 39
Block Diagram of An H.261 Encoder
DCT
Q
Motion
Compensated
Prediction
Motion
Estimation
Buffer
-
SW
IQ
SW
"0"
inter/intra
inter/intra
VLC
Block
type
mc/no mc
Video
In
mc/no mc
+
+
LF
on/off
mc: motion compensated prediction
LF: loop filter
SW: switch, Mux: multiplexer
VLC: variable-length coding
39
VLC
VLC
Mux
IDCT
Intra/
inter

## Slide 40
Block Diagram of An H.261 Decoder
Motion
Compensated
Prediction
VLD
and
Demux
"0"
inter/
intra
mc/
no mc
mv
SW
inter/
intra
mv
mc/
no mc
LF
filter
on/off
40
+
IDCT
IQ
Buffer

## Slide 41
Motion Estimation and Compensation
16 x 16 Block Matching; the search algorithm is not
specified (can be full search, 3-step search, etc. using
mean-absolute-errors, mean-squared-errors, ...)
Motion estimation and compensation is optional in the
encoder
Maximum search range: +/- 15 pixels
Motion vectors are differentially coded with VLC
Motion estimation uses luminance signal only
41

## Slide 42: Coding of Motion Vectors
Differential coding
VLC for MV differences
DMV
...
-7 & 25
-6 & 26
-5 & 27
-4 & 28
-3 & 29
-2 & 30
-1
0
1
2 & -30
3 & -29
4 & -28
5 & -27
6 & -26
7 & -25
...
Code
...
0000 0111
0000 1001
0000 1011
0000 111
0001 1
0011
011
1
010
0010
0001 0
0000 110
0000 1010
0000 1000
0000 0110
...
42

## Slide 43
Quantizer
The number of quantizer is 1 for the INTRA DC coef. and 31 for all other coefficients.
Within a macroblock the same quantizer is used for all coefficients except the INTRA dc one.
The reconstruction levels are defined, but the decision levels are not defined.
The INTRA dc is linearly quantized with a stepsize of 8 and no dead-zone.
Each of the other 31 quantizers is linearly quantized with a central dead-zone and with a step-size of an even value in the range 2 to 62.
43

## Slide 44
Quantizer
T+g/2
T+3g/2
Step-size g
Dead-zone of T for noise removal
T+g/2
T+3g/2
Without dead-zone
T
T+g
44

## Slide 45
2-D VLC
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 … 128
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
…
26
27
…
63
3 5 6 8 9 9 11 13 13 13 13 14 14 14 14
4 7 9 11 13 14 14
5 8 11 13
6 9 13 14
6 11 13
7 11 13
7 13
7 13
8 13
8 14
9 14
9
9
9
11
...
14
EOB: 2 bits (10)
run
Absolute level
Others are 20-bit fixed length codes:
Escape (6 bits) + Run (6 bits) + level (8 bits)
45

## Slide 46: Example
S (sign):
1 negative, 0 positive
Run
Level
Code
EOB
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
2
2
2
2
2
3
3
3
3

1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
1
2
3
4
5
6
7
1
2
3
4
5
1
2
3
4

10
1s If first coefficient in block
11s Not first coefficient in block
0100 s
0010 1s
0000 110s
0010 0110 s
0010 0001 s
0000 0010 10s
0000 0001 1101 s
0000 0001 1000 s
0000 0001 0011 s
0000 0001 0000 s
0000 0000 1101 0s
0000 0000 1100 1s
0000 0000 1100 0s
0000 0000 1011 1s
011s
0001 10s
0010 0101 s
0000 0011 00s
0000 0001 1011 s
0000 0000 1011 0s
0000 0000 1010 1s
0101 s
0000 100s
0000 0010 11s
0000 0001 0100 s
0000 0000 1010 0s
0011 1s
0010 0100 s
0000 0001 1100 s
0000 0000 1001 1s

46

## Slide 47
Macroblock Types
Prediction
Intra
Intra
Inter
Inter
Inter + MC
Inter + MC
Inter + MC
Inter + MC + FIL
Inter + MC + FIL
Inter + MC + FIL
MQUANT
x
x
x
x
MVD
x
x
x
x
x
x
CBP
x
x
x
x
x
x
TCOEFF
x
x
x
x
x
x
x
x
VLC
0001
0000001
1
00001
000000001
00000001
0000000001
001
01
000001
47

## Slide 48
H.261
Does not specify:
  - preprocessing and post processing
  - the criteria for choosing the mode for coding a macroblock
  - the use of BCH (511,493) in the decoder
  - motion estimation in the encoder
  - the quantizer decision levels
  - rate-control algorithm
  - frame-rate
Specifies:
  a macroblock should be forcibly updated at least once per every
  132 times it is transmitted
  - for CIF, the number of bits created by coding any single picture
  must not exceed 256 kb; for QCIF, 64 kb
  - Hypothetical reference decoder (HRD)
48

## Slide 49
Reference Model 8 (RM8)
A specific reference implementation of H.261 encoder
including details, which were not specified in the standard
Motion estimation: +/- 7 pixels, 3-step search
Methods for MC / No MC and Intra / Inter mode
decision
Force Intra-Update (every 132 frames)
Rate control
49
Quantizer stepsize varies from 4 to 64
with increment of 2 depending on the buffer fullness

## Slide 50
Quantizer
T
-T
T+g
T+2g
-T-g
-T-2g
T+g/2
T+3g/2
Stepsize g
Dead-zone of T for noise removal
50

## Slide 51
Decision of Inter/intra
VAR = ((pel - mc_pel)2) / 256
VAROR = ((pel - blk_ave)2) / 256
64
64
Intra
Inter
VAR (variance)
VAROR (variance-original)
Inter mode includes the solid line
Question: reasons for choosing Intra mode?
51

## Slide 52
Decision of MC/no MC
x =
1
0.5
MC on
MC off
x
y
3
1.5
2.7
y = x / 1.1
| bd |
256
| dbd |
256
y =
MC off includes the solid line
bd: block difference, dbd: displaced block difference
52

## Slide 53
Loop Filter
9 | 3 |  |  |  |  |  |  | 
3 | 1 |  |  |  |  |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 2 | 4 | 2 |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 3 | 6 | 3 |  |  | 
Impulse response:
9 | 3 |  |  |  |  |  |  | 
3 | 1 |  |  |  |  |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 2 | 4 | 2 |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 1 | 2 | 1 |  |  | 
 |  |  | 3 | 6 | 3 |  |  | 

## Slide 54
Loop Filter (Cont.)
without loop filter
loop filter
128 kbps
128 kbps
64 kbps
64 kbps
54

## Slide 55
Rate Control
Buffer size = q * 6.4 kb (100ms)
Quantization step size varies from 4 to 64 with step 2
When the buffer fullness exceeds q*6.4 kb, the coefficients
and the motion vectors are set to zero in the next MB
Buffer Fullness
< 400*q
< 600*q
< 800*q
< 6200*q
>= 6200*q
Quantizer Step Size
6
8
62
64
...
...
4
55

## Slide 56: MPEG-1
56

## Slide 57
History of MPEG-1 Standard
Applications
  Video on digital storage media
  Computer and telecommunication networks
57
For basic digital storage media application
Video
en-
coder
Audio
en-
coder
Storage
Editing
Storage
Trans-
port
Storage
Video
de-
coder
Audio
de-
coder

## Slide 58
Parameters of MPEG-1
Picture size up to 4096 × 4096 supported
  Normally at 360 × 240
Pel aspect ratio: 14 choices
Picture rates: 23.976, 24 (movies), 25 (PAL), 29.97, 30, 50, 59.94, 60
4:2:0 format(macro block比例)
  (same as H.26x)
= Y Pels
= Cb and Cr pels
= Block Edges
58

## Slide 59
Typical MPEG-1 Video Source Format
Signal component
352
176
176
Format
Luminance (Y)
Chrominance (Cb)
Chrominance (Cr)
240/288
120/144
120/144
SIF (525/625)
Lines/Frame
Pixels/Line
Uncompressed bit-rate for transmitting SIF at 30 fps
is 30.4 Mb/s
59

## Slide 60
Forward, backward, or average prediction: one or two motion vectors per 16x16 block with half-pixel accuracy
Bi-directional Motion Estimation
Current B-picture
Backward motion vector
Past reference picture
Future reference picture
Forward motion vector
Best matching macroblock
Best matching macroblock
60

## Slide 61
Coding Structure of GOP
I = Intra-Picture Coding, allow random access, for reference
P = Predictive coding, causal prediction only, can be referenced
B = Bi-directional coding, noncausal prediction, never referenced
I
I
I
B
B
B
B
B
B
B
B
B
B
P
P
P
B
B
P
Group of pictures
Group of pictures
61
Random access可以從任意地方播，就會從此處找尋最近的I開始

## Slide 62
I-Pictures
DCT coded without reference to any other pictures
Stored in a frame buffer in encoder and decoder
Used as basis of prediction for entire GOP
I
B
B
P
B
B
P
B
B
P
B
B
I
Time
I Picture
All these P and B pictures depend on
the preceding I picture
62

## Slide 63
P-Pictures
DCT coded with reference to the preceding anchor picture
Stored in a frame buffer in encoder and decoder
Use forward prediction only
I
B
B
P
B
B
P
B
B
P
B
B
I
Time
This P picture depends on
this I picture
Forward Prediction
This P picture depends on
this P picture
63

## Slide 64
B-Pictures
DCT coded with reference to either the preceding anchor picture, the following anchor picture(ref. pic), or both
Use forward, backward or bi-directional prediction
I
B
B
P
B
B
P
B
B
P
B
B
I
Time
This B picture
depends on
this I picture and this P picture
Bi-directional Prediction
This B picture
depends on
this P picture and this P picture
64

## Slide 65: GOP Rules
A GOP must contain at least one I picture
This I picture may be followed by any number of I and P pictures
Any number of B pictures may occur between anchor pictures, and B pictures may precede the first I picture
A GOP, in coding order, must start with an I picture
A GOP, in display order, must start with an I or B picture and must end with an I or P picture
65
=>delay

## Slide 66: Regular and Irregular GOPs
Regular GOP’s are defined by N and M*:
  N is the I picture interval
  M is the anchor picture interval. There are M-1 B pictures between anchor pictures
Irregular GOP’s are not defined by N and M, but are still allowed as long as they follow the GOP Rules.
Regular: N=1, M=1
(12 GOP’s shown)
I
B
B
B
I
P
P
B
B
B
B
B
B
B
B
I
P
P
P
B
B
B
B
B
B
B
B
I
P
P
P
All GOP’s in Display Order
Regular: N=6, M=2
(2 GOP’s shown)
Regular: N=12, M=3
(1 GOP shown)
Irregular
I
I
I
I
I
I
I
I
I
I
I
B
B
B
I
P
P
*N and M are not MPEG
syntax elements and are
not used in any way by
the specification.
66

## Slide 67: GOP Picture Orderings
Two Distinct Picture Orderings
  Display Order (input to encoder, output of decoder)
  Coding Order (output of encoder, input to decoder)
  These are different if B frames are present
  B frames must be reordered so that “future” anchor pictures are available for prediction.
GOP
Display Order
Input to Encoder
B
B
B
B
B
B
B
B
I
P
P
P
GOP
Coding Order
Output of Encoder
B
B
B
B
B
B
B
B
I
P
P
P
GOP
Display Order
Output of Decoder
B
B
B
B
B
B
B
B
I
P
P
P
67

## Slide 68: Six Hierarchical Layers of MPEG
Sequence
(Display Order)
GOP
(Display Order,
N=12, M=3)
Picture
Slice
Macroblock
Y
4
5
0
1
2
3
Y Blocks
B
B
B
B
B
B
B
B
I
P
P
P
68
Note: Y = Luma =Red-Y =Blue-Y
Block
Block

## Slide 69: Six Hierarchical Layers of MPEG (Cont.)
• Important syntax elements in each layer:
Sequence Picture Size; Frame Rate
Bit Rate; Buffering Requirements
Programmable Coding Parameters
GOP Random Access Unit
SMPTE Time-Code
Picture Timing information (buffer fullness, temporal reference), Coding type (I, P, or B)
Slice Intra-frame addressing information
Coding re-initialization (error resilience)
Macroblock Basic coding structure, Coding method, Motion Vectors, Quantization
Block DCT coefficients
69

## Slide 70
Video sequence
Picture
Slice
Macroblock
...
...
...
...
Sequence header
GOP
GOP
GOP
GOP
Sequence end code
GOP header
Picture
Picture
Picture
Picture header
Slice
Slice
Slice
Slice header
Macroblock
Macroblock
Macroblock
Macroblock header
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Differential DC coefficient
Sequence layer
GOP layer
Picture layer
Slice layer
Macroblock layer
Block layer
AC coefficient
AC coefficient
AC coefficient
End-Of-Block
...
MPEG-1 Video Bit-stream
70

## Slide 71
MPEG Bit-Stream Structure
Sequence
Header
Sequence
Sequence
Picture
width
Picture
height
Aspect
ratio
Bitrate
Picture
rate
...
GOP
Header
Picture
Header
Picture
Picture
Header
Picture
...
Temporal
Reference
Picture
Type
VBV
Delay
Extension
Start Code
Picture
Structure
...
...
Sequence
Header
Sequence layer
GOP layer
71

## Slide 72
MPEG Bit-Stream Structure (Cont.)
Picture layer
Slice layer
Macroblock layer
Block Layer
Picture
Header
Slice
Header
Macroblock
Macroblock
Slice
Header
Macroblock
...
Address
Type
Quantizer
Scale
Coded
Block
Pattern
Block
Block
Motion
Vectors
...
...
Macroblock
Block
Slice
72

## Slide 73
Slice Structure
A slice is a collection of macroblocks in raster scan order.
A slice in MPEG-1 video frame can be single MB or entire picture.
73

## Slide 74
Macroblock Structure
4:2:0
4:2:2
4:4:4
0
1
2
3
4
Y
5
0
1
2
3
4
Y
5
0
1
2
3
Y
6
7
4
5
6
7
8
10
9
11
12 Blocks
8 Blocks
6 Blocks
luma
chroma
Spatial Sampling Relationship
MPEG-1
chroma
MPEG-2
chroma
74

## Slide 75
  Quantization
Intra(I pic)
(nearest integer)
Nonintra(P/B pic)
(rounded down)
Same as H.263
original
quantized
original
quantized
Quantization
without dead zone
Quantization
with dead zone
75

## Slide 76
  Quantization Example
DC
35
1
2
1
0
0
0
0
3
2
-1
0
0
0
0
0
1
0
-1
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Quantizer Scale
QS = 40
(from Rate Controller)
Quantized DCT Coefficients
T’[u][v]
DCT Frequency
Coefficients
T[u][v]
Default Intra
Quantization Matrix
QM[u][v]
A/B
A
B
Pointwise
Division
and Rounding
Note: Quantization of DC term
is fixed and does not depend
on QM or QS.
DC
8
16
19
22
26
27
29
34
16
16
22
24
27
29
34
37
19
22
26
27
29
34
34
38
22
37
40
32
35
40
48
58
34
38
46
56
69
27
29
35
38
46
56
69
83
22
26
27
29
34
22
26
27
29
32
35
40
48
26
27
29
26
27
29
QS
DC
276
59
89
39
7
-13
-12
-7
137
-94
-35
4
17
16
7
2
51
25
-42
-20
-14
1
5
7
-12
-5
-5
-4
0
2
-1
0
12
0
-4
-2
1
-6
2
-6
6
8
-5
-1
0
40
-8
-16
-4
-4
-8
3
17
-13
5
-7
0
-1
2
14
14
-1
-3
-2
16
76

## Slide 77
  Default Quantization Matrices
Intra Matrix: QMI[u][v]
Note: AC coefficients (all coefficients
except DC) are first multiplied by 16,
then divided by QS*QMI[u][v].
DC term is treated specially.
8
16
19
22
26
27
29
34
16
16
22
24
27
29
34
37
19
22
26
27
29
34
34
38
22
37
40
32
35
40
48
58
34
38
46
56
69
27
29
35
38
46
56
69
83
DC
22
26
27
29
34
22
26
27
29
32
35
40
48
26
27
29
26
27
29
Non-Intra Matrix: QMN[u][v]
Note: All coefficients are first
multiplied by 16, then divided
by QS*QMN[u][v].
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
77

## Slide 78
  Downloadable Quantization Matrices
Example of
Downloadable Matrix
(TM5 Non-Intra Matrix)
16
17
18
19
20
21
22
23
24
25
27
28
30
31
33
17
18
19
20
21
22
23
24
18
19
20
21
22
23
26
24
19
20
21
22
23
27
26
25
20
21
22
23
28
27
26
24
21
22
23
30
28
27
26
24
22
23
31
30
28
27
25
24
23
For improved quality in certain coding situations, quantization matrices for Intra and Non-Intra macroblocks can be downloaded.
The decoder uses these instead of the defaults (which are not sent in the bitstream)
The example at right shows an improved Non-Intra Quant Matrix used by the MPEG-2 Test Model 5 (TM5)
78

## Slide 79
  Quant Matrix Effect
DC
“freq”
Before Quantization
“freq”
After Quantization
Reconstruction Levels
DC
“freq”
Before Quantization
“freq”
After Quantization
Reconstruction Levels
Flat Matrix
Tilted Matrix
79

## Slide 80
  2-D VLC
Similar to H.261
  Most codes same, some codes shorter
  Levels up to 255

## Slide 81
MPEG-1 Video Coding Standard
Similar to H.261, MPEG-1 specifies
- Bit stream syntax and semantics
- Decoding to raster representation
- VBV (video buffer verifier)
doesn't specify
- Pre-processing to raster representation
- Encoding
- Post-processing from raster representation
Left flexible (parameters in the bit stream)
- Coded bit-rate (constant or variable)
- Lines per picture (< 4096)
- Pels per line (< 4096)
- Picture rate (24, 25, or 30 per second)
- Pel aspect ratio (14 choices)
81

## Slide 82
Simulation Model 3 (SM3)
A specific reference implementation of MPEG-1
encoder including details which were not specified
in the standard
Motion estimation: one forward and/or one backward
vector per MB with half-pixel resolution; 2-step search:
(1) full search in the range of +/- 7 pixels, (2) search 8
neighboring half-pel positions
Methods for MC / No MC and Intra/Inter decision
Quantizer, rate control
82
一個方法決定是否使用motion compensate / intra等等，通常使用於此block可能是新的，對於計算(mvx,mvy)及residue會比直接intra該block還差，就可能使用該block進行intra計算即可（減少傳輸量)，rate control則是看buffer狀況調整quantization step size以控制輸出量

## Slide 83: MPEG-2
83

## Slide 84
MPEG-2 Video Coding Standard
Primarily for coding interlaced video at 4 - 15 Mb/s for digital broadcast TV and high quality digital storage Media; also for HDTV, cable/satellite TV, video services over networks (e.g., ATM), and 2-way communications
MPEG only specifies bitstream syntax and decoding process
Encoding algorithms (e.g., motion estimation, rate Control and mode decisions) are open to invention and proprietary techniques
MPEG is asymmetric in that much less computational power is required in the decoder.
84
Encoding的computation花費>>decoding的
相反：distributed system(ex. Sensor)就會變成decoding那邊計算量大

## Slide 85
Features
Picture quality - good quality NTSC (4-6 Mb/s)
excellent quality NTSC (8-10 Mb/s)
Random access/channel switching in limit time - intra-pictures
Trick modes - basic VCR functions
Delay - low delay mode using Simple Profile for visual communications
Error resilience - intra-mv, data-partitioning, priority assignment to video
layers
Allow higher chroma resolution - e.g., 4:2:2 and 4:4:4
Scalability - data partition, SNR scalability, spatial scalability,
temporal scalability, hybrid scalability (up to 3 layers)
Compatibility - decodes MPEG-1 bit-stream, base layer may be decoded
by MPEG-1 decoder
Support multiple video formats and frame rates
Subset of the standard permit real-time encoders of reasonable complexity
Scalability縮小原圖，並再次放大，這個過程會有誤差，因此可以與原圖相減得到residue，網路好就basic和residue一起送，反之就送basic就好
若支援mpeg2，就也要支援mpeg1

## Slide 86
SP
MP
SNRP
SSP
HP
Each profile supports groups of features for an application area
Simple Profile: low-delay videoconferencing
Main Profile: most important, for general applications
SNR Profile: multiple grades of quality
Spatially Scalable Profile: multiple grades of quality and resolution
High Profile: multiple grades of quality, resolution, and chroma format
Profiles and Applications
New profiles:
4:2:2 profile
Multiview profile
86

## Slide 87
Profiles and Levels (Cont.)
Level
Profile
Simple
4:2:0
Main
4:2:0
SNR
Scalable
4:2:0
Spatially
Scalable
4:2:0
High
4:2:0 or
4:2:2
High
1920x1152
(60 frames/s)
High-1440
1440x1152
(60 frames/s)
Main
720x576
(30 frames/s)
Low
352x288
(30 frames/s)
10.4 Ms/s
15 Mbit/s
62.7 Ms/s
80 Mbit/s
47 Ms/s
60 Mbit/s
10.4 Ms/s
15 Mbit/s
3.04 Ms/s
4 Mbit/s
10.4 Ms/s
15 Mbit/s
for 2 layers
47 Ms/s
60 Mbit/s
for 3 layers
100 Mbit/s
for 3 layers
3.04 Ms/s
4 Mbit/s
for 2 layers
80 Mbit/s
for 3 layers
20 Mbit/s
for 3 layers
* numbers in the table are maximum allowed
87

## Slide 88
MPEG-2: Resolutions and Formats
Picture sizes extension up to 16kx16k; 720x480 ~ TV resolution
Support picture rates: 23.98, 24, 25, 29.97, 30, 50, 59.94, 60
Support both progressive and interlaced formats
Support 4:2:0, 4:2:2, and 4:4:4 sampling formats
88

## Slide 89
Chrominance Sampling
4:2:2
4:4:4
4:2:0
89

## Slide 90
Chrominance Sampling (Cont.)
t
i
m
e
t
i
m
e
t
i
m
e
interlaced 4:2:0
interlaced 4:2:2/4:4:4
progressive
top
field
bottom
field
top
field
bottom
field
90

## Slide 91
MPEG-2 Slice Structure
A slice is a collection of macroblocks in raster scan order.
Restriction on slice sizes:
  MPEG-2 restricts a slice to be contained within a row of macroblocks
MPEG-2 allows gaps between slices in “general slice structure”
MPEG-2 defines “restricted slice structure,” in which no gaps are allowed. This is used in most Profiles and Levels.
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
W
V
X
Y
Z
Example of
restricted slice structure
91
Mpeg1 slice任意，mpeg2則最多只能一整條

## Slide 92
Interlaced Video Coding
Frame-pictures or field-pictures
Motion compensation
  Frame prediction for frame-pictures (same as MPEG-1)
  Field prediction for field-pictures
  Field prediction for frame-pictures
  Dual-prime
    Field-pictures or frame-pictures
    Only for P-pictures
  16×8 MC for field pictures
Same except bitstream
92

## Slide 93
Allowable Prediction Modes
Field Pictures
Field Prediction
16x8 Motion
Compensation
Dual Prime
Frame Pictures
Field Prediction
Frame Prediction
Dual Prime
93

## Slide 94
16
16
16
8
Frame/Field Motion Compensated Predictive Coding
94

## Slide 95
Prediction Modes
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
frame
1
1
frame
2
2
reference
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
x
x
o
o
frame
1
1
frame
2
2
reference
Field Prediction
x
x
x
x
x
x
x
x
o
o
o
o
o
o
o
o
x
x
x
x
x
x
x
x
o
o
o
o
o
o
o
o
dv1
dv2
dv2
v
field1 field2 field1 field2
Dual Prime Prediction
dmv
dmv
Frame Prediction
(a)
(b)
(c)
reference
v
95

## Slide 96
Frame & Field predictions
16x16
16x16
Reference Frame
Predicted Frame
Frame Prediction
Best 16x16 region in reference picture determines frame MV for 16x16 MB. Only mode allowed in MPEG-1.
16x8
16x8
16x8
Field Prediction
Best 16x8 region in top or bottom field in reference picture determines field MV’s for top and bottom portions of 16x16 MB.
Current MB
Top Field of Current MB
Bottom Field of Current MB
16x8
16x8
16x8
or
or
Top
Field
Bottom
Field
96

## Slide 97
Dual-Prime Prediction
In Frame Pictures
Single MV (heavy arrow) sent in bitstream; this represents predictions from fields of same parity. Small differential MV’s are also sent; these represent offset predictions from fields of opposite parity. Same and opposite field predictions are averaged to form final prediction for each 16x8 region of current MB.
Reference Frame
Predicted Frame
16x8
16x8
16x8
16x8
Top Field of Current MB
Bottom Field of Current MB
16x8
16x8
Average
Top
Field
Bottom
Field
Average
In Field Pictures
Single MV (heavy arrow) sent in bitstream; this represents prediction from field of same parity. A small differential MV is also sent; this represents an offset prediction from field of opposite parity. Same and opposite field predictions are averaged to form final prediction for current 16x16 MB.
First
Field
Second
Field
Average
16x16
This Field not
yet decoded.
16x16
16x16
97

## Slide 98
Dual-Prime Prediction (Cont.)
Top
Bottom
Reference
Picture
Predicted
Picture
Vector Transmitted
in Bitstream for
Same Parity Fields
Top
Bottom
Differential Vector
Transmitted
in Bitstream
(limited to values
-1, 0, +1)
Vector Derived
at Decoder
for Opposite
Parity Fields
98

## Slide 99
Prediction Modes
PSNR at 4 Mbits/s
  Frame-pictures, M=1
  Frame-pictures, M=3
  Field-pictures, M=1
99

## Slide 100
Low Delay Coding
For face-to-face applications
Total encoding and decoding delay of less than 150 ms can be achieved
Low delay coding by not using B-pictures, using dual-prime prediction for P-frames, intra slices, skip frames
100

## Slide 101
Frame/Field DCT
Frame format
Field format
101

## Slide 102
Frame/Field Adaptive DCT
Organize 1616 block as frame blocks or filed blocks
Compute correlation in vertical direction in each case
Choose the case that has higher correlation
Frame blocks
Field blocks
102

## Slide 103
Frame/Field Adaptive DCT (Cont.)
PSNR (dB) at 4 Mbits/s
  M=1
  M=3
103

## Slide 104
Progressive/Interlaced Scan
Zigzag (progressive)
Alternate (interlaced)
104
(dB)
(dB)
因為field DCT這樣做導致關係跑掉了，因此不能再使用zigzag scan

## Slide 105
Quantization Tools
Quantization Matrix (QM)
  8x8 matrix can be shaped so that coarser quantization of high spatial frequencies occurs
  coarser quantization of high spatial frequencies saves bits but causes little or no subjective degradation
  In MPEG-2, up to four QM’s (luma intra/non-intra and chroma intra/non-intra) can be changed at the picture rate
  Default matrices are specified and need not be sent, but different ones can be downloaded
Quantizer Scale (QS)
  QS can change on a macroblock basis
  rate control’s job is to modify QS in a way that keeps picture quality high for a given bit rate
105
mpeg1 QS都一樣，mpeg2則可以各自不同

## Slide 106
MPEG-2 Quantizer Scale Types
quantizer_scale_code [1, 31]
(sent in bitstream)
Linear
Quantizer Scale
(q_scale_type = 0)
Nonlinear
Quantizer Scale
(q_scale_type = 1)
106

## Slide 107
2-D VLC (Inter/Intra)
107
(FLC)
內縮的原因：motion vector較準確，讓residue變小->length下降

## Slide 108
2-D VLC (Intra)
(FLC)

## Slide 109
Coding for DC
Range larger then MPEG1
109

## Slide 110
Test Model 5 (TM5)
- Frame/field/dual prime and forward/backward ME
- Integer pel full search followed by half-pel search
- MPEG-1 mode decision: MC/no MC, inter/intra
- MPEG-1 and nonlinear quantizer tables
- Zigzag scan for inter; alternate scan for intra coding
- Quantizer and rate control
110

## Slide 111
Scalability Types
Data partitioning
SNR scalability
Spatial scalability
Temporal scalability
Hybrid scalability
111

## Slide 112
Data Partitioning
  May cause picture drift
  I-pictures can clean up the drift, but cause higher bit rates
  One of the limitations in data partitioning is the need for a high allocated bit rate to the base layer to avoid “blockiness”
  The simplest kind of scalability, has no extra complexity over the nonscalable encoder
DC
priority
break
point
enhancement
layer data
base layer
data
112

## Slide 113
Spatial Scalable Encoder
Video
in
Lower level
coded
bitstream out
Upper level
coded
bitstream out
DCT
+
IDCT
-
+
MCP
VLC
Q
IQ
DCT
+
IDCT
-
+
MCP
VLC
Q
IQ
W
113

## Slide 114
Spatial Scalable Decoder
VLD
IQ
IDCT
MCP
VLD
IQ
IDCT
+
MCP
+
Lower level
coded
bitstream in
Lower level
decoded
video out
Upper level
decoded
video out
Upper level
coded
bitstream in
W
114

## Slide 115
SNR Scalable Encoder
DCT
+
IDCT
+
-
+
-
+
MCP
Q
VLC
VLC
Q
Video
in
IQ
Lower level
coded
bitstream out
Upper level
coded
bitstream out
IQ
coarse
Q
fine
Q
115
QP大->粗糙(例如先送0 3 6 9 12 15…)
與lower相反，送0-3之間有什麼、3-6之間有什麼…

## Slide 116
SNR Scalable Decoder
VLD
IQ
IDCT
MCP
+
VLD
IQ
IDCT
+
MCP
+
Upper level
coded
bitstream in
Upper level
decoded
video out
Lower level
decoded
video out
Lower level
coded
bitstream in
coarse
Q
fine
Q
116

## Slide 117
Applications of Scalability
Data partitioning (simplest):
  Video over low-loss networks (e.g., ATM with congestion control)
SNR scalability:
  Transmission of video at different qualities
    multiquality video, video on demand, broadcasting of TV and enhanced TV
  Video over networks with high error or packet loss rates
    the Internet,
    heavily congested ATM networks
117

## Slide 118
Applications of Scalability
Spatial scalability (most complex):
  Interworking between two different standard video codecs or heterogeneous data networks
  Simulcasting of drift-free, good-quality video at two spatial resolutions, such as standard TV and HDTV
  Distribution of video over computer networks
  Video browsing
  Reception of good quality low spatial resolution pictures over mobile networks
  Similar to other scalable coders, transmission of error resilient video over packet networks.
118

## Slide 119
Error Resilience
Slice structure
Concealment motion vectors
Data partition
SNR scalability
Spatial scalability
Temporal scalability
Intra pictures
Intra slices
119
送1 3 5 7 9…，中間用平均重建
當然有誤差->enhancement時是用residue送(例如送2 4 6 8 10等等)

## Slide 120
MPEG Average Quality
120

## Slide 121
3:2 Pull Down
MPEG-2 provides a mechanism for film-originated content to be coded at 24 frame/sec but displayed at 30 frames/sec
The lower frame rate of film means it can be coded at the same quality as 30 frame/sec video, but at a lower bit rate.
The repeat_first_field (rff) and top_field_first (tff) flags allow decoders to recreate the 3:2 pulldown sequence for display.
1/24 sec
1/30 sec
1/60 sec
Film Frames
coded as progressive
frames at 24 frames/sec
3:2 pulldown alternately
creates 3 and 2 displayed
fields for each input frame
rff=1
tff=1
rff=0
tff=0
rff=1
tff=0
rff=0
tff=1
repeat
first field
repeat
first field
121
解決電影(24)到電視(30)的frame rate問題

## Slide 122
Pan-and-Scan
16:9
Reconstructed
Frame
4:3
Display
Rectangle
In this example the horizontal
frame center offset is a positive number.
MPEG-2 provides a mechanism for panning a display rectangle around a reconstructed frame
Horizontal and vertical offsets are specified to 1/16 pixel resolution and can be sent for every displayed field.
This allows widescreen material to be viewed on 4:3 displays.
frame_centre_horizontal_offset
122
Flicking：閃爍，pixel不連續
Retargeting：轉變size(透過抽絲剝繭)

## Slide 123: H.263 & H.263+
123

## Slide 124
H.263: ITU-T Very Low Bit Rate Video Coding
ITU-T SG16/LBC Near Term
Optimized at bitrate < 22 kb/s (overall < 28.8 kb/s)
TMN5:
- 3-4 dB higher PSNR than H.261 at < 64kb/s for all ITU
test sequences
- 30% saving compared with MPEG1 SM3 at 512 kb/s
for “football” at CIF resolution
124

## Slide 125
Picture Formats Supported
Uncompressed bitrate(Mbps)
10 frames/sec
30 frames/sec
Picture
format
Luminance
pixels
Luminance
lines
H.261
support
H.263
support
Mono
Color
Mono
Color
SQCIF
128
96
No
Yes
1.0
1.5
3.0
4.4
QCIF
176
144
Yes
Yes
2.0
3.0
6.1
9.1
CIF
352
288
Optional
Optional
8.1
12.2
24.3
36.5
4CIF
704
576
No
Optional
32.4
48.7
97.3
146.0
16CIF
1408
1152
No
Optional
129.8
194.6
389.3
583.9
125

## Slide 126: H.263 Input Formats
Sub-QCIF (128x96), QCIF, CIF, 4CIF (704x576), 16 CIF (1408x1152)
Encoder shall be able to support either sub-QCIF or QCIF
Decoder shall be able to support both sub-QCIF and QCIF
GOB 0
GOB 0
GOB 1
GOB 1
GOB 2
GOB 2
GOB 3
GOB 3
GOB 4
GOB 4
GOB 5
GOB 5
GOB 6
GOB 6
GOB 7
GOB 7
GOB 8
GOB 8
GOB 9
QCIF
GOB 10
GOB 11
GOB 12
GOB 0
GOB 13
GOB 1
GOB 14
GOB 2
GOB 15
GOB 3
GOB 16
GOB 4
GOB 17
GOB 5
CIF
sub-QCIF
126

## Slide 127
H.263: Main Features wrt H.261
Half-pixel motion estimation (range -16 to 15.5) with motion vector prediction
Four negotiable options:
- Unrestricted motion vector: motion vectors can point outside the picture,
maximum range for motion vectors: -31,5 to 31.5 instead of -16 to 15.5
- Advanced prediction mode: 8x8 motion vectors, overlapped block motion
compensation (OBMC), motion vector can point outside the picture
- Syntax-based arithmetic coding (about 5% decrease in bit-rate)
- PB-frame mode (similar to dual-prime motion estimation)
Reduced overhead: optional GOB header and BCH, 3-D VLC
Different VLC tables at macroblock and block levels
127
OBMC:平均左右的結果，避免blocking effect

## Slide 128
Coding control
Source
coder
Video multiplex
coder
Transmission
buffer
Receiving
buffer
Video multiplex
decoder
Source
decoder
Video
signal
Coded
External control
a) Video coder
b) Video decoder
Block Diagram of Video Codec
128

## Slide 129
Differential Motion Vector
MV2
MV1
MV
MV3
MV2
(0,0)
MV
MV3
MV1
MV1
MV
MV1
MV2
MV1
MV
(0,0)
: Picture or GOB border
MVDx=MVX-PX
MVDY=MVY-PY
PX=Median(MV1X,MV2X,MV3X)
PY=Median(MV1Y,MV2Y,MV3Y)
PX=PY=0 if MB is INTRA coding
129
送差值

## Slide 130
Advanced Prediction Mode
Four 8x8 vectors instead of one 16x16 vector
MV3
MV
MV3
MV1
MV
MV1
MV1
MV
MV2
MV
MV3
MV1
MV2
MV3
MV2
MV2
Differential motion vector
130

## Slide 131
Advanced Prediction Mode (Cont.)
Adjacent
block
Adjacent
block
Adjacent
block
Current luminance block
Adjacent
block
131

## Slide 132
Advanced Prediction Mode (Cont.)
Overlapped block motion compensation for P-frames:
each pixel in a prediction block is a weighted sum of
three prediction values (blocks pointed by motion vectors
of current, top/bottom, left/right)
Motion vectors can point outside the picture
4 5 5 5 5 5 5 4
5 5 5 5 5 5 5 5
5 5 6 6 6 6 5 5
5 5 6 6 6 6 5 5
5 5 6 6 6 6 5 5
5 5 6 6 6 6 5 5
5 5 5 5 5 5 5 5
4 5 5 5 5 5 5 4
2 2 2 2 2 2 2 2
1 1 2 2 2 2 1 1
1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1
1 1 2 2 2 2 1 1
2 2 2 2 2 2 2 2
2 1 1 1 1 1 1 2
2 2 1 1 1 1 2 2
2 2 1 1 1 1 2 2
2 2 1 1 1 1 2 2
2 2 1 1 1 1 2 2
2 2 1 1 1 1 2 2
2 2 1 1 1 1 2 2
2 1 1 1 1 1 1 2
weighting
Top/bottom
Left/right
132

## Slide 133
Syntax-Based Arithmetic Coding (SAC) Mode
Arithmetic coding is used instead of VLC
Cumulative frequencies are provided
About 5% less bits at the same SNR
133
給定freq並在傳輸時一定的時間去update freq

## Slide 134
TMN6
Test model near-term 6
- Advanced motion prediction (AP)
- Half-pel motion accuracy
- Overlapped block motion compensation
- Adaptive motion vectors for 8x8 or 16x16
- Syntax-adaptive arithmetic coding (SAC)
- PB frames
134

## Slide 135
Foreman at 12.5 fps
Performance Comparison of H.263 & H.261
135

## Slide 136
Performance Comparison of H.263 & H.261 (Cont.)
Foreman
at 12.5 fps
64 kbps
136

## Slide 137
Foreman at 12.5 fps
Performance Comparison of H.263 w/wo AP Mode
137

## Slide 138
Performance Comparison of H.263 w/wo SAC Mode
Foreman at 12.5 fps
138

## Slide 139
Performance Comparison of H.263 w/wo PB Mode
Foreman at 12.5 fps
139

## Slide 140
Performance Comparison of H.263 w/wo All Options
Foreman at 12.5 fps
140

## Slide 141: H.263+
Formally H.263 Version 2
Enhancements of H.263
12 new negotiable modes
Backward compatible with H.263
Allows a wide range of custom source formats
141

## Slide 142: Custom Source Formats
Higher picture clock frequency (PCF)
Custom picture formats
Custom pixel aspect ratios (PAR)
142
Pixel aspect ratio | pixel width : pixel height
Square | 1:1
CIF | 12:11
525-type for 4:3 picture | 10:11
CIF for 16:9 picture | 16:11
525-type for 16:9 picture | 40:33
Extended PAR | m:n, m and n are relatively prime

## Slide 143: H.263+ Optional Modes
Annex D: New Unrestricted Motion Vector Mode (UMV)
Annex I: Advanced Intra Coding Mode
Annex J: Deblocking Filter Mode
Annex M: Improved PB-Frame Mode
Annex O: Temporal, Spatial, and SNR Scalability Mode
Annex P: Reference Picture Resampling Mode
Annex Q: Reduced Resolution Update Mode
Annex S: Alternative Inter VLC Mode
Annex T: Modified Quantization Mode
Annex K: Slice Structured Mode
Annex R: Independent Segment Decoding Mode
Annex N: Reference Picture Selection Mode
Error resilience:
143

## Slide 144: New Optional Modes for Coding Efficiency Improvement
Coding efficiency
  New UMV mode
  Advanced Intra Coding Mode
  Alternate Inter VLC Mode
    Use intra table for inter DCT
  Deblocking Filter Mode
    Depending on quantization step size
  Modified Quantization Mode
    More flexible changes of quantization step sizes
    Finer quantization for chrominance
    Extended DCT range
  Improved PB-Frame Mode
    Forward, backward, or bi-directional
144

## Slide 145: Modifications to UMV Modes
Single value VLC
  Easy implementation
Reversible VLC table
  Better error resilience
Larger motion vector range
  Depending on the picture size
  Up to [–256, 255.5]
145

## Slide 146: Advanced Intra Coding
Current Block
A separate VLC table for intra DCT
Modified inverse quantization
Spatial prediction of DCT coefficients
  DC only, vertical DC & AC, horizontal DC & AC
146

## Slide 147: Advanced Intra Coding (Cont.)
If the prediction refers to the horizontally adjacent block => alternate-vertical scan
If the prediction refers to the vertically adjacent block
=> alternate-horizontal scan
Alternate (vertical)
Alternate (horizontal)
147

## Slide 148: Advanced Intra Coding (Cont.)
148

## Slide 149: Modified Quantization Mode
149

## Slide 150: Deblocking Filter Mode
150

## Slide 151: Deblocking Filter Mode (Cont.)

## Slide 152: Reference Picture Selection Mode
DCT
Q
IDCT
Motion
compensated
prediction
IQ
_
+
+
VLC
Buffer
APn
AP1
AP2
.
.
.
AP: additional
picture memory
Motion
estimation
Video in
Coded
video
out
152

## Slide 153: Spatio-Temporal Error Propagation with RPS
N（negative）ACK 第4張decode後發現嚴重錯誤，因此return給encoder說這邊錯，encoder就會讓現在在弄的frame去ref.錯誤前面一個frame避免一直錯下去
V.S. ACK只要對的就return，因此沒return的就是錯誤

## Slide 154: Scalability
Scalability
  Decode partial information from partial bitstream
  To fit various bandwidth requirements
  To fit terminals with different capabilities
Scalability Modes
  Temporal scalability: bi-directional prediction
  Spatial scalability
  SNR scalability
154

## Slide 155: Temporal Scalability (Cont.)

## Slide 156: Spatial Scalability (Cont.)
156

## Slide 157: SNR Scalability (Cont.)
157

## Slide 158: Reference Picture Resampling
Global motion compensation
Rotating motion
Special-effect warping
MV
00
MV
0V
MV
H0
MV
HV
158

## Slide 159: Supplemental Enhancement Information
Enhanced features
  Picture freeze and release
  Tagging information
    Snapshot
    Video segment start/end
    Progressive refinement start/end
  Chroma key
Can be discarded by decoders that do not understand
159

## Slide 160: Chroma Key
A video sequence f(x,n) with regions Ri
For each region Ri, replace the non-object area with a special color C0
C0
160

## Slide 161: Computational Complexity Comparison of Optional Modes
161

## Slide 162
TMN8
Motion estimation and mode selection
Rate control algorithm
  Frame skipping
    If the buffer fullness is larger than a threshold M, the encoder
    skips encoding frames until the buffer fullness is below M.
  Frame-layer rate-control
    Frame target bits selection: the target bits is selected
    depending on the buffer fullness
  Macroblock-layer rate control
    Initialization: calculating the standard deviations si for all MBs
    Compute Q for i-th MB according to si and encode the
    macroblock
    Update counters and model parameters
162

## Slide 163
H.263++ New Features
Annex U: Fidelity enhancement by macroblock and block-level reference picture selection – a significant improvement in compression quality
Annex V: Packet loss & error resilience using data partitioning with reversible VLCs
163

## Slide 164
H.263++ New Features (Cont.)
Annex W:additional supplemental enhancement information
  IDCT mismatch elimination (specific fixed-point fast IDCT)
  Arbitrary binary user data
  Text messages (arbitrary, copyright, caption, video description, and URI)
  Error resilience:
    Picture header repetition (current, previous, next+TR, next-TR)
    Spare reference pictures for error concealment
  Interlaced field indications (top & bottom)
164
當原本平滑時，會因為經過DCT.IDCT而導致誤差，又因DCT為整數，導致mismatch

## Slide 165
H.263++ Performance: Annex U
0
20
40
60
80
100
120
140
160
26
28
30
32
34
36
Bit-Rate [kbps]
PSNR [dB]
TMN-10
50
10
3 reference pictures
H.263 combined with
Long-Term Memory Prediction
17 %
Foreman
10 Hz, QCIF
100 frames encoded
165

## Slide 166
H.263++ Average Bit-rate Saving
Number of
Reference Frames
Average
Bit-Rate
Savings
in [%]
@ 34 dB
1
2
3
5
10
17
33
65
100
0
10
20
30
40
Foreman
Container
Mobile & Calendar
Stefan
Mother & Daughter
Silent
Tempete
Average
13.5 %
166

## Slide 167: MPEG-4
167

## Slide 168
MPEG-4
  Initial driving application:
  1. Video coding for very low bit-rate video
  2. Object-based coding
  MPEG-4 attempts to become THE standard for streaming AV media on the Internet and via wireless networks
  Error-resilience features, optimized for low-bit-rate applications, fine granular scalability (FGS) coding
  MPEG-4 file format defines first standard for streaming AV media on the Internet
168
object-based （需要image/video segmentation->ill-posed problem）所以bad vs其他的用block-based （導致mpeg4比較不盛行）

## Slide 169
MPEG-4 Video Object Plane (VOP)
VOP1
VOP2
VOP3
169

## Slide 170
170
Integration of Natural and Synthetic Content

## Slide 171: MPEG-4 Video: Core & Generic Coder
171

## Slide 172
Coding of AV Objects
AV scenes consist of “objects”
Objects can be natural or synthetic (A&V, text & graphics, animated faces, arbitrarily shaped or rectangular)
A “compositor” composes objects in a scene (A&V, 2 & 3D)
Binary format for scenes: BIFS
172

## Slide 173
VOP-Based Encoding
VOP1
VOP2
VOP3
content-based
bitstream access
& manipulation
content-based
scalability
video objects
segmentation
& object mask
layered encoding
separate decoding
bitstream
(VOP3)
bitstream
(VOP2)
bitstream
(VOP1)
173

## Slide 174
MPEG-4 Video Encoder
MUX
Shape
Coding
Motion
Estimation
Texture
Coding
Motion
Compensation
Previous Reconstructed VOP
Buffer
Shape information
Texture
information
VOP_of_arbitrary_shape
Motion
information
174

## Slide 175: VOP Decoder
Shape
Decoding
Texture
Decoding
Shape Information
D
E
M
U
L
T
I
P
L
E
X
E
R
Motion
Compensation
Bitstream
Motion
Decoding
VOP
Memory
Reconstructed
VOP
Compositor
Video Out
Compositing script
175

## Slide 176: Texture Coding (1/3)
Motion compensated DCT
  Very similar to H.263
Polygon matching
macroblock
transparent pixels
pixels for polygon matching
VOP
176

## Slide 177: Texture Coding (2/3)
VOP
macoblock
partially outside VOP
(
blocks partially outside
the VOP are coded
by DCT after padding)
macroblock
entirely
outside
VOP (not coded)
macroblock
entirely inside
VOP
(
coded by
conventional
DCT scheme)
177

## Slide 178: Texture Coding (3/3)
Variable
Length
Decoding
Motion
Compensa-
tion
Inverse
Scan
Inverse
Quantiz-
ation
Inverse
DCT
VOP
Memory
Reconstructed
VOP
Decoded
Shape
Coded
Data
QFS[n]
SQF[v][u]
F[v][u]
f
[y][x]
d[y][x]
Decoded
Pels
Inverse
AC/DC
prediction
QF[v][u]
178

## Slide 179: Adaptive DC Prediction
A
B
C
D
X
Macroblock
Y
or
or
179

## Slide 180: Adaptive AC Prediction
A
B
X
D
C
o
r
Y
o
r
macroblock
180

## Slide 181: Scanning Pattern
Alternate-horizontal scan
Alternate-Vertical scan
Zig-Zag scan
DC
DC
DC
181

## Slide 182: Motion Estimation/Compensation (1/3)
182

## Slide 183: Motion Estimation/Compensation (2/3)
P-VOP or
B-VOP
modified block
(
polygon) matching
conventional
block matching
no
matching
reference
P-VOP or
I-VOP
padded reference
pixels for block
matching
reference VOP
pixels for block
matching
padded reference
pixels for
unrestricted
block matching
bounding
box
advanced
prediction
mode
183

## Slide 184: Shape Adaptive DCT for Texture Coding
184

## Slide 185: Shape Coding
Binary shape
  Context-based arithmetic encoding (CAE)
Gray scale alpha plane
  Motion compensated DCT
    Similar to texture coding
Gray-level
Alpha
support
Binary
shape coder
texture
Texture
Coder
185

## Slide 186: Block-based CAE
The context
Inter
Intra
BAB: binary alpha block
 | C9 | C8 | C7 | 
C6 | C5 | C4 | C3 | C2
C1 | C0 | ? |  | 
C3 | C2 | C1
C0 | ? | 
Pixel fo the current
BAB
 | C8 | 
C5 | C6 | C7
 | C4 | 
aligment
Pixel fo the bordered
MCBAB

## Slide 187
+
Sprite Coding
187

## Slide 188: Warping of Reference Sprite
Sprite and sprite points
VOP and reference points
(
x’
3
,y’
3
)
(
x’
1
,y’
1
)
(
x’
2
,y’
2
)
(
x’
0
,y’
0
)
(
x
3
,y
3
)
(
x
2
,y
2
)
(
x
1
,y
1
)
(
x
0
,y
0
)
Sprite Image
Actual Frame
Only 2-8 global motion
parameters are transmitted
per frame
188
8 tie points帶入，得到8個equation

## Slide 189: Static Sprite Coding Tools
Based sprite coding
Low latency sprite coding
Scalable sprite coding
Shape/Texture
Decoding
Shape/Texture
Decoding
Warping Vector
Decoding
Sprite
Buffer
Warping
VOL
Bitstream
VOP
Bitstream
Reconstructed
Samples
189

## Slide 190: MPEG-4 Video verification model
Verification model (VM8)
  Video object plane (VOP) structure
  Polygonal matching for motion estimation
  Padding
  Motion/texture coding derived from H.263
  Binary and gray-scale shape coding
  B-VOPs (video object plane) derived from H.263 B-pictures and MPEG-1/2 B-pictures
190

## Slide 191: SNHC
Synthetic & Natural Hybrid Coding (SNHC)
  To provide efficient representation and composition of synthetically and naturally generated audiovisual data
  Compression of geometry, integration of mixed media, synthetic and spatial audio, facial and body animation
  Applications
  Virtual environment, conferencing, education/entertainment, media production, and real-time interactive and broadcast media experiences
191

## Slide 192
MPEG-4 Visual Face Animation
Application:
- very low rate video (as low as 100 b/s)
- user interface to intelligent agents
Model-based coding of faces
Models are not normative
Type of data:
- Facial definition parameter
- Facial animation parameter
- Rendering
192

## Slide 193
MPEG-4 Visual Face Animation
193

## Slide 194
MPEG-4 Visual Mesh Coding
Used to code and animate 2D/3D objects
Mesh is a set of connected polygons
Image and video can be rendered onto mesh
Error robustness
Mesh + still texture -> synthetic video
Mesh is modified by motion vectors transmitted for each node
194

## Slide 195
2-D Mesh Coding
Decoding process
Mesh
Geometry
Decoding
Mesh
Motion
Decoding
Mesh
Data
Memory
Variable
Length
Decoding
Coded
Data
Decoded
Mesh
dx
n
dy
n
ex
n
ey
n
x
n
y
n
t
m
195

## Slide 196
3-D Mesh Coding
Progressive representation
  Streaming of 3D objects
  Both spatially and temporally
Indexing and retrieval of 3D meshes
  Multiresolution databases
  Related to MPEG-7
196

## Slide 197
Wavelet for Scalable Texture Coding
Decompose the signal in the frequency domain
Critical downsampling maintains the number of samples in the subbands
For 2D case, separable filters are often used. Decompose into four bands: LL, LH, HL, HH
Decompose the LL band iteratively
H
2
(z)
Highpass
2
H
1
(z)
Lowpass
2
CODEC 1
CODEC 2
2
2
F
1
(z)
F
2
(z)
Lowpass
Highpass
197
對水平用low pass垂直用high pass（依此類推），並縮小1/4並拼接四塊，最重要的就是LL

## Slide 198
Wavelet for Scalable Texture Coding (Cont.)
“Zero Tree”
198

## Slide 199
MPEG-4 Visual Still Texture Coding
Wavelet image coder
Intended for rendering of mesh and face objects
Fine granularity scalability (FGS) supported
Error robustness
199
FGS：準備enhancement部分與base-layer部分，根據網路提供部分多寡

## Slide 200
Resync
Marker
MB
Address
Quant.
Param.
Header
Extenion
Temporal
Reference
Texture
DATA
Motion
DATA
Motion
Marker
Shape
DATA
Error
Burst
Texture Data
Reversible VLC
Forward decoding
Backward decoding
Resync marker can be placed at any MB boundary (resync
with MB address) (e.g. resync evenly spaced in bit-stream)
Separating motion vectors and the texture data with resync
RVLC (reversible variable length coding)
HEC (header extension code)
Error Resilience Tools
200

## Slide 201
Error Resilience Tools- Resync Marker
Picture Start Code
MPEG-4 Resync Marker
H.263 Resync Marker
H.263 Birstream
MPEG-4 Bitstream
201

## Slide 202
MPEG-4 Fine Granularity Scalability (FGS)
Internet applications
broadcast applications over packet networks
- Low complexity
- Supports both unicast & multicasting capabilities
- Supports various layers of SNR enhancements
- Covers a “range” of bitrates instead of a few discrete bitrates
- Base-layer compatible to MPEG-4
- Error robustness
202

## Slide 203
FGS Encoder
Adaptive Quantization
Bitplane coding
DCT
Q
Q-1
IDCT
Motion
Compensation
Motion
Estimation
Frame
Memory
VLC
Input Video
Base Layer
Bitstream
Shift
Bitplane
Find
Maximum
Bit-plane
VLC
Enhancement
Bitstream
FGS Enhancement Encoding
Clipping
203
細緻化是在8個bit planes，選擇是否加入該bit plane（9種選擇）

## Slide 204
FGS Decoder
VLD
Q
-1
IDCT
Motion
Compensation
Frame
Memory
Bit-plane
VLD
IDCT
FGS Enhancement Decoding
Base Layer
Bitstream
Enhancement
Bitstream
Base Layer Video
(optional Output)
Enhancement Video
Clipping
Bit-plane
Shift
Clipping
204

## Slide 205
205
VISUAL TOOLS:
Basic (I-VOP, P-VOP,
AC/DC Prediction, 4-MV,
Unrestricted MV)
Error Resilience
Short Header
B-VOP
P-VOP with OBMC
(Texture)
Method 1/2 Quantization
P-VOP based temporal
scalability (rectangular,
arbitrary shaped)
Binary Shape
Gray Shape
Interlace
Sprite
Temporal Scalability
(rectangular)
Spatial Scalability
(rectangular)
N-Bit
Scalable Still Texture
2D Dynamic Mesh with
uniform topology
2D Dynamic Mesh with
Delaunay topology
Facial Animation
Parameters
Simple Core Main Simple N-Bit Hybrid Basic Still Simple
Scalable Animated Scalable Face
Texture Texture
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Profiles:

## Slide 206: Profiles
Profiles:
Simple: H.263-like
Simple Scalable: Simple + rectangular scalability
Core: Simple + binary shape + scalability
Main: Core + gray shape + interlace + sprite
...
206

## Slide 207
Coding Efficiency (MAIN Profile)
(optimized headers, VLC tables)
- 30 % reduction in bitrate compared to MPEG-1
(tested between 40-768 kbit/s)
Coding Efficiency (Advanced Coding Eff. Profile (ACE))
(with global motion estimation)
- 30-50% reduction in bitrate compared to MAIN Profile
(218 - 1000 kb/s) (critical sequences)
Performance Baseline
207

## Slide 208
Universal Multimedia Access (UMA)
Any Network:
  wireline or wireless
  circuit-switched or packet-switched
  symmetrical or asymmetrical
  broadband or bandwidth-limited
  LAN, MAN or WAN
Any Terminal:
  various processing capability
  various storage capability
  various display capability
Any Where:
  seamless ubiquitous access
208

## Slide 209: MPEG-7
209
mpeg-7是for multimedia database(content-based retrival)，not for video/image compression ，將輸入轉成可以描述的樣子

## Slide 210: Scope of MPEG-7
applications
Analysis
(automatic or manual)
Feature extraction is outside MPEG-7
Search and query are outside MPEG-7
Feature Extraction
Standard Description
Scope of MPEG-7
A/V Data
Search Engine
210

## Slide 211: MPEG-7: Multimedia Content Description Interface
To define standardized solutions that allow users or
agents to search, browse, filter audiovisual content.
User
Search Engine
Image Database
input
query
(MPEG-7)
visualization of result images
human
in the
loop
user feedback
user categories
211

## Slide 212: MPEG-7: Multimedia Content Description Interface (Cont.)
Text
How can “Non-Text-Information” be described in a useful
way?
Speech- and Audio-Descriptors
        Pitch
        Melody
        Frequency
        Sex of speaker
Visual Clues
  Texture
  Color
  Form and Shape (2D/3D)
  Motion Activity
  Higher Order Object-Models
  Persons, Gestures
212

## Slide 213: Concepts in MPEG-7
Data
Feature: e.g., color, motion
Descriptor (D): e.g., histogram, motion vectors
  Mapping between representation values and the feature
  Basic unit of a description scheme
Description Scheme (DS)
  A framework that defines the descriptors and their relationships
Description
  An instantiation of a DS
  Combination of descriptors and DS’s
213

## Slide 214: Descriptors (D’s)
Color histograms
Dominant colors
DCT coefficient color description
Color composition (local)
Gabor wavelet (global)
Edge descriptor (Local)
Shape
Contour
Camera motion (global)
Object motion (Local)
MB motion activity (local and global)
...
214

## Slide 215: Color Histogram
215

## Slide 216: Color Composition
Image Data
Query
216

## Slide 217: What MPEG7 Standardize?
Description Definition
Language (DDL)
Descriptors
Description Schemes
Flexible description
of description schemes
or descriptors
- XML Schema
Relations between
descriptors
- shape + motion
- shape + frame no
- Text,
- Color, Texture
- Shape, Motion
- Pitch, Melody
217

## Slide 218: Example Uses
Music
  Play a few notes on a keyboard or whistle a melody
  Retrieve a list of musical pieces that are similar
Graphics
  Draw a few lines on a screen
  Retrieve a set of images containing similar graphics
Images
  Define objects, including color patches or textures
  Retrieve examples among which you select the interesting objects to compose your image
218

## Slide 219: Example Uses (Cont.)
Movement
  On a given set of objects, describe movements and relations between objects
  Retrieve a list of animations fulfilling the described temporal and spatial relations
Scenario
  On a given content, describe actions and get a list of scenarios where similar actions happen
Voice
  Using an excerpt of Pavarotti’s voice to retrieve a list of Pavarotti’s records or video clips
219

## Slide 220: MPEG-4 AVC/H.264
220

## Slide 221: Design Goals of MPEG-4 AVC
High compression efficiency
Flexible application to delay constraints appropriate to a variety of services
Error resilience capability
Complexity scalability
Full specification of decoding (no mismatch)
High quality application
Network friendliness
221

## Slide 222: Video Coding Hierarchy
Sequence, consisting of
Pictures, consisting of
Slices, consisting of
Macroblocks, consisting of
Blocks, consisting of
Pixels / pels
Note: for interlaced video, a picture consists of either one frame or two fields
NAL
VCL
222

## Slide 223: The Features of VCL (1/3)
Transformation
  Integer 4x4 block transform for residual coding
  Hardamard
    A 4x4 transform on the DC coefficients of the 4x4 blocks in a 16x16 macroblock
    A 2x2 transform for the DC coefficients of the 4x4 chroma blocks in a 8x8 macroblock
223
Motion Estimation
  Variable block-size motion prediction (7 block sizes: 16x16, 8x8, 4x4, 16x8, 8x16, 8x4, 4x8)
  Integer, 1/2-, and 1/4-pixel motion vector accuracy
  Multiple reference frames (max. 15) may be used for prediction

## Slide 224: The Features of VCL (2/3)
Entropy coding:
  Context-based adaptive variable length coding (CAVLC)
  Context-based adaptive binary arithmetic coding (CABAC)
Others:
  Space-domain Intra prediction (10 prediction modes)
  De-blocking loop filter
  Motion vector prediction
  Slice structure
  Interlace coding tools
224

## Slide 225: Frame Types
I-frame
P-frame
B-frame
SP- and SI-frames
  SP and SI frames provide functionalities for bit-stream switching, splicing, random access, VCR functionalities, and error resilience/recovery
225

## Slide 226: Picture Formats
Color sequences using 4:2:0 chroma sub-sampling
interlaced frames
progressive frames
...
.
.
.
.
.
.
= Location of luminance sample
= Location of chrominance sample
Guide:
Time
Top
Field
Bottom
Field
Top
Field
= Luminance Sample
= Chrominance Sample
226

## Slide 227: Macroblock Subdivision
Each picture is divided into 16x16 macroblocks.
The order of the macroblocks in the bitstream depends on the macroblock allocation map (MAM) and is not necessarily raster scan order
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9

## Slide 228: MPEG-4 AVC/H.264: Encoder Architecture
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
228

## Slide 229: MPEG-4 AVC/H.264: Motion Compensation
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
Motion vector accuracy 1/4 (6-tap filter)
8x8
0
4x8
0
1
0
1
2
3
4x4
8x4
1
0
8x8
Types
0
16x16
0
1
8x16
MB
Types
8x8
0
1
2
3
16x8
1
0
229

## Slide 230: Motivation of Variable Block-Size Coding
230

## Slide 231: Motion Compensation
Various block sizes and shapes for motion compensation
1/4 sample accuracy
  6 tap filtering to 1/2 sample accuracy
  simplified filtering to 1/4 sample accuracy
  special position with heavier filtering
Multiple reference pictures
Temporally-reversed motion and generalized B-frames
B-frame prediction weighting
231

## Slide 232: Block Modes of P Pictures
Macroblock: 16x16
7 motion prediction modes
  16x16, 16x8, 8x16, 8x8, 8x4, 4x8, 4x4
  Motion vectors accuracy: integer, ½-, and ¼-pixel
0
0
1
1
0
0
1
2
3
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Mode 1
Mode 2
Mode 3
Mode 4
Mode 5
Mode 6
Mode 7
232

## Slide 233: Motion Vector Search
Motion Mstimation
  Integer pixel search
  Fractional pixel search (1/2- and 1/4-pixel)
  Reference frames selection from multiple reference frames (max. 15 frames)
  Search range:
    horizontal [-2048, 2047.75] (max)
    vertical [-512, 511.75] (max)
233

## Slide 234: Motion Estimation
Motion vector prediction
  In same slice
  Median prediction (except 16x8 and 8x16 blocks)
A, B, C, D and E may come from different reference picture
C is not available,
B,C, and D are not available,
Any predictor is neither of above two rules, its MV is 0.

## Slide 235: Motion Estimation
Motion vector prediction for 16x8 and 8x16 blocks
  Directional segmentation prediction
8x16
16x8
235

## Slide 236: Motion Estimation
Integer pixel search
  search positions are organised in a “spiral” structure around the predicted vector
. . . . . .
. 15 9 11 13 16
. 17 3 1 4 18
. 19 5 0 6 20
. 21 7 2 8 22
. 23 10 12 14 24
236

## Slide 237: Motion Estimation
full fractional-pixel search (1/2- and ¼-pixel)
a
b
c
d
e
f
g
h
I
II
III
IV
V
VI
VII
VIII
C
H
1
H
2
V
1
V
2
D
1
D
2
D
3
D
4
Capital letters (C,H1,H2…) : integer pixel positions
Roma numbers (I,II,III...): 1/2-pel positions
Lower case letters(a,b,c...):1/4-pel positions
237

## Slide 238: Motion Estimation
Fractional pixel search
  Check the eight 1/2-pel candidates, I ~ VIII around the best integer-pel C; decide the best 1/2-pel V subject to the minimal cost among the 1/2-pel candidates
  Check the eight 1/4-pel candidates, a ~ h around the best 1/2-pel V, decide the best 1/4-pel h subject to the minimal cost among the 1/4-pel candidates
  Select the motion vector and block-size pattern, which produces the lowest cost
238

## Slide 239: Fractional Pel Value Interpolation: Luma
Calculate half-pel values
  use 6-tap filter {1, -5, 20, 20, -5, 1} to get b
  = clip(((b+16)>>5))
  c from b values using the 6 tap filter
  = clip(((c+512)>>10))
Average of integer and half-pel values to find d, e, f, g
  e.g., d = (A+ )>>1
h = (+ )>>1 (diagonal direction averaging)
i = (A1+A2+A3+A4+2)>>2
239

## Slide 240: Fractional Pel Value Interpolation: Chroma
are the fractional position in units of one eighth samples
A, B, C, and D are integer pixels
A
B
C
D
2
2
/
)
2
/
)
(8
)
(
)
)(
((
8
8
D
d
d
C
d
d
B
d
8
d
A
d
8
d
8
v
y
x
y
x
y
x
y
x
+
+
-
+
-
+
-
-
=
240

## Slide 241: B-Pictures
Advantages:
  Improve coding efficiency
  Provide temporal scalability
5 modes:
  Direct mode: derived forward and backward MVs, none transmitted
  Forward mode: prediction from a previous reference frame
  Backward mode: prediction from a subsequent reference frame
  Bi-directional mode: separate forward and backward MVs
  Intra prediction mode
MVs in direct mode:
  MVF = (TRB * MV)/TRD
  MVB = (TRB - TRD) * MV/TRD
P/I
P
B
MV
MV
F
MV
B
Time
TR
D
TR
B
241

## Slide 242: B-Pictures
Direct Mode
  No MV data is transmitted
  Same block structure as co-located MB in temporally subsequent picture
  MVs are computed as scaled version of corresponding MV of the co-located MB
I
0
B
1
B
2
B
3
P
4
B
5
B
6
B
7
P
8
242

## Slide 243: B-Pictures
Z = (TDB  256)/ TDD MVF = (Z  MV +128) >> 8
W= Z – 256 MVB = (W MV +128) >> 8
f0
f1
f1
f0
f1
f0
TD
D
TD
B
MV
Time
MV
F
MV
B
...
...
current block
co-located block
List 1 Reference
List 0 Reference
Current B
243

## Slide 244: Mode Decision
Block difference
  Diff(i,j) = Original(i,j) - Prediction(i,j)
SAD and SATD
  DiffT means apply Hadamard transform to Diff
Prediction
Block_difference
Hadamard transform
SA(T)D
SA(T)Dmin
Loop for prediction mode decision
Integer-pel search
244

## Slide 245: Mode Decision
Given the last decoded frames, Lagrange multipliers
and the MB quantisation parameter .
(Note: for B or SP frame is 4 times as much as that for I or P frame.)
245

## Slide 246: Mode Decision
Choose intra prediction modes for the Intra 4x4 macroblock mode by minimizing with
Determine the best Intra16x16 prediction mode by choosing the mode that results in the minimum SATD.
246

## Slide 247: Mode Decision
For each 8x8 sub-partition
  Perform motion estimation and reference frame selection by minimizing SSD + L x Rate(MV, REF)
  B frames: Choose prediction direction by minimizing SSD + L x Rate(MV(PDIR), REF(PDIR))
  Determine the coding mode of the 8x8 sub-partition using the rate-constrained mode decision, i.e. minimize SSD + L x Rate(MV, REF, Luma-Coeff, block 8x8 mode)
Here the SSD calculation is based on the reconstructed signal after DCT, quantization, and IDCT
247

## Slide 248: Mode Decision
Perform motion estimation and reference frame selection for 16x16, 16x8, and 8x16 modes by minimizing
B frames: determine prediction direction by minimizing
248

## Slide 249: Mode Decision
Choose the MB prediction mode by minimizing
I:
P:
B:
“skip mode” refers to the 16x16 mode, where no motion and residual information are encoded
249

## Slide 250: MPEG-4 AVC/H.264: Intra Prediction
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
Directional spatial prediction
(9 types for luma, 1 chroma)
e.g., Mode 3: diagonal down/right prediction a, f, k, p are predicted by (A + 2Q + I + 2) >> 2
1
2
3
4
5
6
7
8
0
Q A B C D E F G H
I a b c d
J e f g h
K i j k l
L m n o p
M
N
O
P
250

## Slide 251: Intra Prediction: 4x4 Luma Blocks
Mode 0: vertical prediction
Mode 1: horizontal prediction
Mode 2: DC prediction
Mode 3: Diagonal down/left prediction
Mode 4: Diagonal down/right prediction
Mode 5: vertical-left
Mode 6: horizontal-down
Mode 7: vertical-right
Mode 8: horizontal-up
DC prediction:
pred() = Average of pixels A, B, C, D, E, F, G, and H
I A B C D
E a b c d
F e f g h
G i j k l
H m n o p
Mode 0
I A B C D
E a b c d
F e f g h
G i j k l
H m n o p
Mode 1
0
1
4
3
5
7
8
6
251

## Slide 252: Intra Prediction: 4x4 Luma Prediction
252

## Slide 253: Intra Prediction: 16x16 Luma Blocks
Mode 0: vertical
Mode 1: horizontal
Mode 2: DC
Mode 3: plane
  Be used only if all neighboring samples are available
Pred() = Clip( ),
where
(x,y)
253

## Slide 254: Intra Prediction: 16x16 Luma Blocks
……..
……..
Mean(H+V)
H
V
254

## Slide 255: MPEG-4 AVC/H.264: Transform Coding
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
4x4 block integer transform
Main profile: adaptive block size transform (8x4,4x8,8x8)
Repeated transform of DC coeffs for 8x8 chroma and 16x16 Intra luma blocks
255

## Slide 256: Transform Coding: Luma DC
Luma DC in Intra_16x16 MB using Hadamard transformation
Forward transform:
Inverse transform:
//2

## Slide 257: Transform Coding: Chroma DC
Chroma DC in 8x8 block Hadamard transformation
  Forward transform
  Inverse transform
257

## Slide 258: Transform: Luma and Chroma residual
Luminance and chrominance 4x4 residual blocks
Forward transform
Inverse Transform
258

## Slide 259: Quantization/Dequantization (1/2)
Scan order
  4x4 residual and 4x4 luma DC block
  2x2 chroma DC block
    raster order
0
1
5
6
2
4
7
12
3
8
11
13
9
10
14
15
259

## Slide 260: Quantization/Dequantization (2/2)
QP: 0 ~ 51
: QP for luma coefficients
: QP for chroma coefficients
  QPC for chroma is determined from the current value of
QPY | <30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
QPC | =QPY | 29 | 30 | 31 | 32 | 32 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | 37 | 38 | 38 | 38 | 39 | 39 | 39 | 39
260

## Slide 261: MPEG-4 AVC/H.264: Multiple Reference Frames
Entropy
Coding
Motion
Data
Deq./Inv. Transform
Motion-
Compensated
Predictor
Control
Data
Quant. Transf. coeffs
0
Intra/Inter
Coder
Control
Decoder
Motion
Estimator
Transform/ Quantizer
-
Multiple Reference Frames for
Motion Compensation
261

## Slide 262: MPEG-4 AVC/H.264: Residual Coding
Entropy
Coding
Deq./Inv. Transform
Motion-
Compensated
Predictor
Control
Data
Quant. Transf. coeffs
Motion
Data
0
Intra/Inter
Coder
Control
Decoder
Motion
Estimator
Transform/ Quantizer
-
Residual coding is based on 4x4 blocks
Integer transform
262

## Slide 263: Residual and Intra Coding
EXACT MATCH simplified transform
  Based primarily on 4x4 transform (all prior standards: 8x8)
  Requires only 16 bit arithmetic (including intermediate values)
  Expanded to 8x8 for chroma by 2x2 transform of the DC values
  Easily extensible to 10-12 bits per component
Adaptive block transform sizes for main profile
Intra coding structure
  Directional spatial prediction (10 types luma, 1 chroma)
  Expanded to 16x16 for luma intra by 4x4 transform of the DC values
263
T=

## Slide 264: Quantization and Deblocking
Quantization of transform coefficients
  Logarithmic step size control
  Extended range of step sizes
  Smaller step size for chroma (per H.263 Annex T)
  Table-driven
Reconstruction is 16-bit multiply, add, shift
In-loop deblocking filter
264

## Slide 265: Deblocking Filter
Boundaries in a macroblock to be filtered (luma boundaries shown with solid lines and chroma boundaries shown with dotted lines)
Vertical edges
(chroma)
Vertical edges
(luma)
Horizontal edges
(luma)
Horizontal edges
(chroma)
16*16 Macroblock
16*16 Macroblock
265

## Slide 266: Deblocking Filter
Content dependent boundary filtering strength
  For each boundary between neighbouring 4x4 luma blocks, a “boundary strength” Bs is assigned
  If Bs=0, filtering is skipped for that particular edge
  In all other cases, filtering is dependent on the local sample properties and the value of Bs
266

## Slide 267: Deblocking Filter
Flowchart to determine boundary strength Bs
Block boundary
between block p and q
Block p or q
intra coded or
slice type is SI or SP
?
Bs=3
Block boundary
is also Macroblock
boundary
?
Coefficients
coded in block
p or q
?
Bs=2
Bs=4
|V
1
(p,x) - V
1
(q,x)| >= 1 or
|V
1
(p,y) - V
1
(q,y)| >= 1 or
if bi-predictive
|V
2
(p,x) - V
2
(q,x)| >= 1 or
|V
2
(p,y) - V
2
(q,y)| >= 1
Bs=0
(skip)
Bs=1
YES
NO
YES
YES
NO
NO
Block p and q have
different reference frames
or a different number of
reference frames?
YES
NO
YES
NO
267

## Slide 268: Deblocking Filter
Thresholds for each block boundary
  Set of samples across this edge are only filtered if Bs ≠ 0 && |p0 – q0| <  && |p1 – p0| <  && |q1 – q0| < 
   and  are determined by IndexA and IndexB, respectively, where
  IndexA = Clip3(0, 51, QPav + Filter_Offset_A)
  IndexB = Clip3(0, 51, QPav + Filter_Offset_B)
  Filter_Offset_A and Filter_Offset_B used to modify filter characteristics
Clip3( a, b, c) =
p3
p2
p1
p0
q0
q1
q2
q3
268
QPav：QP average

## Slide 269: Deblocking Filter: Bs < 4
269
  If ,
  If ,
  is determined by IndexA and Bs

## Slide 270: Deblocking Filter: Bs = 4
Left/upper side
If ap <  && |p0 – q0| < (( >> 2) + 2) (A)
  P0 = ( p2 + 2*p1 + 2*p0 + 2*q0 + q1 + 4) >> 3
  P1 = ( p2 + p1 + p0 + q0 + 2) >> 2
In the case of luma filtering,
  P2 = ( 2*p3 + 3*p2 + p1 + p0 + q0 + 4) >> 3
Otherwise, if the condition of Eq. (A) does not hold,
  P0 = ( 2*p1 + p0 + q1 + 2) >> 2
270

## Slide 271: Deblocking Filter: Bs = 4
Right/lower side
If aq <  && |p0 – q0| < (( >> 2) +2) (B)
  Q0 = ( p1 + 2*p0 + 2*q0 + 2*q1 + q2 + 4) >> 3
  Q1 = ( p0 + q0 + q1 + q2 + 2) >> 2
In the case of luma filtering,
Q2 = ( 2*q3 + 3*q2 + q1 + q0 + p0 + 4) >> 3
Otherwise, if the condition of Eq. (B) does not hold,
  Q0 = ( 2*q1 + q0 + p1 + 2) >> 2
271

## Slide 272: Deblocking Filter
1) without filtering 2) with H264/AVC deblocking
272

## Slide 273: Entropy Coding
Entropy
Coding
Inv. Scal. & Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
273

## Slide 274: Variable Length Coding
Exp-Golomb code is used for all symbols except for transform coefficients
Context adaptive VLCs coding of transform coefficients
  No end-of-block, but number of coefficients is decoded
  Coefficients are scanned backwards
  Contexts are built dependent on transform coefficients
274

## Slide 275: Content-based Adaptive Binary Arithmetic Coding (CABAC)
Usage of adaptive probability models for most symbols
Exploiting symbol correlations by using contexts
Restriction to binary arithmetic coding
  Simple and fast adaptation mechanism
  Fast binary arithmetic codec based on table look-ups and shifts only
Average bit-rate saving over CAVLC 10-15%
275

## Slide 276: SP/SI Frame
SP frame
  motion-compensated predictive coding
  similar to P
  SP allows identical reconstruction even when different reference pictures are being used
SI frame
  spatial prediction
  similar to I
  SI allows identical reconstruction to a corresponding SP
provide functionalities for bitstream switching, splicing, random access, VCR functionalities such as fast-forward, and error resilience/recovery
276

## Slide 277: SP/SI Frame: Bitstream Switching
Bitstream 1
Bitstream 2
S
2
S
1
P
P
P
P
P
P
P
P
S12
277

## Slide 278: SP/SI Frame: Bitstream Splicing
Bitstream 1
Bitstream 2
S
2
S
1
P
P
P
P
P
P
P
P
SI2
278

## Slide 279: Profiles
Baseline profile
Extended profile
Main profile
279

## Slide 280: Baseline Profile
I and P picture types
In-loop deblocking filter
1/4-sample motion compensation
VLC-based entropy coding: CAVLC
4:2:0 Chrominance format
Field pictures (for Level 2.1 and above)
use 15 or fewer reference frames
have a compression ratio per picture of 4:1 or greater
280

## Slide 281: Extended Profile
Bi-predictive slices
SP and SI slices
Weighted prediction
All features in baseline profile are included
281

## Slide 282: Main Profile
CABAC
Interlaced pictures
All features in baseline profile are included
282

## Slide 283: Level Definitions
Level # | Max Picture Size (MBs) | Max Video Bitrate (1000 bits/sec) | Horizontal MV Range (full pels) | Vertical MV Range (full pels) | Minimum luma Bi-predictive block size
1 | 99 | 64 | [-2048, 2047.75] | [-64, 63.75] | 8x8
1.1 | 396 | 128 | [-2048, 2047.75] | [-128, 127.75] | 8x8
1.2 | 396 | 768 | [-2048, 2047.75] | [-128, 127.75] | 8x8
2 | 396 | 2000 | [-2048, 2047.75] | [-128, 127.75] | 8x8
2.1 | 792 | 4000 | [-2048, 2047.75] | [-256, 255.75] | 8x8
2.2 | 1620 | 4000 | [-2048, 2047.75] | [-256, 255.75] | 8x8
3 | 1620 | 8000 | [-2048, 2047.75] | [-256, 255.75] | 8x8
3.1 | 3600 | 20000 | [-2048, 2047.75] | [512, 511.75] | 8x8
3.2 | 5120 | 20000 | [-2048, 2047.75] | [512, 511.75] | 8x8
4 | 8192 | 20000 | [-2048, 2047.75] | [512, 511.75] | 8x8
5 | 19200 | TBD | [-2048, 2047.75] | TBD | 8x8
283

## Slide 284: Complexity of H.264 Codec Design
Codec design includes relaxation of traditional bounds on complexity (memory & computation) – rough guess 2-3x decoding power increase relative to MPEG-2, 3-4x encoding
Problem areas:
  Smaller block sizes for motion compensation (cache access issues)
  Longer filters for motion compensation (more memory access)
  Multi-frame motion compensation (more memory for reference frame storage)
  More segmentations of macroblock to choose from (more searching in the encoder)
  More methods of predicting intra data (more searching)
  Arithmetic coding (adaptivity, computation on output bits)
284

## Slide 285: Performance Comparison
Test of different standards
Using same rate-distortion optimization techniques for all codecs
Streaming test: high-latency (included B frames)
Real-time conversation test: no B frames
Several video sequences for each test
Compare four codecs:
  MPEG-2
  H.263 MPEG-4
  JVT/H.26L/AVC (with & without B pictures)
285

## Slide 286: Coding Efficiency Comparison
27
28
29
30
31
32
33
34
35
36
37
38
39
0
50
100
150
200
250
Bit-rate [kbit/s]
Foreman QCIF 10Hz
Quality
Y-PSNR [dB]
MPEG-2
H.263
MPEG-4
JVT/H.264/AVC
286

## Slide 287: Conclusions
Video coding layer is based on hybrid video coding and similar in spirit to other standards
New key features are:
  enhanced motion compensation
  small blocks for transform coding
  improved deblocking filter
  enhanced entropy coding
Bit-rate savings generally 50% or better against any otherstandard for the same perceptual quality
Increased complexity relative to prior standards
Standard of both ITU-T VCEG and ISO/IEC MPEG
287