## Slide 1
Chapter 1. Introduction

## Slide 2: Digital Media World
Many devices
Wired or wireless
Access from anywhere
Software Integration
Personalized delivery
Rich Services

## Slide 3: Visual Communication Applications (1/4)
Applications driving the technology
Visual communication needs evident from paintings in ancient caves

## Slide 4: Visual Communication Applications (2/4)
Remote collaborations
Videophone at Home
PC, LAN,
Wireless, POTS,
ISDN, ADSL,
Cable Modem,
…
PC-based videophone at office
Monitoring/
Elder care
Network

## Slide 5: Visual Communication Applications (3/4)
One-way applications
Video streaming, video on demand, Video broadcasting,
Video email, Video surveillance, Digital TV, HDTV, DVD,
VCD, Digital camera, Digital camcorder, Digital VCR,
Games, …
Limitation: Bandwidth
Two-way applications
Videophone, Videoconferencing, Distance learning,
Remote collaboration, Games, …
Limitations: Bandwidth, End-to-end Delay

## Slide 6: Visual Communication Applications (4/4)
Multimedia appliances, streaming server, hardware/software codecs, embedded systems, ASICs, IP, media processors, PC cards, applications software, authoring tools, Indexing and retrieval software systems, …
Support many hardware and software products:

## Slide 7
Overview of Video Coding Techniques

## Slide 8: Video Coding Standards
  Every standard was developed with an initial driving-application which may be different from the current driving applications
  The requirements from the driving-applications determined how the standard was developed
  Current driving applications determine how the standards will evolve
  The application ultimately determines if the standard will be successful
  ITU-T vs. ISO

## Slide 9
Some Video Coding Standards
Specify only the decoder(encoder跟著變)
Standardize the minimum

## Slide 10
JPEG

## Slide 11: JPEG
  Driving application: image compression for storage
  Technology: Integration of existing techniques
  discrete cosine transform (DCT) and entropy coding

## Slide 12: Discrete Cosine Transform (DCT)
8x8 DCT
basis functions

## Slide 13: Entropy Coding
Input sequence:
0,0,-3,5,1,0,-2,0,0,0,0,2,
-4,3,-2,0,0,0,1,0,0,-2
Run-length sequence:
(2,-3)(0,5)(0,1)(1,-2)(4,2)
(0,-4)(0,3)(0,-2)(3,1)(2,-2)
Run-length Coding:

## Slide 14: JPEG: DCT + Quantization + Entropy Coding
DCT+ Quantization + Variable-Length Coding
DCT
Quantization
(step size = 30)
IQ, IDCT
Mean Square Error = 38.75
Motion compensated
difference block
IDCT
Z








33
-
1
1
1
1
0
0
0
-
2
1
0
-
1
0
0
0
0
5
1
-
1
0
0
0
0
0
2
0
-
1
0
0
0
0
0
-
1
0
1
0
0
0
0
0
0
1
2
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
994
-
34
20
38
22
0
5
-
1
-
49
17
8
-
17
-
4
-
1
4
-
2
149
35
-
37
-
15
1
3
-
1
-
4
58
8
-
32
-
3
-
9
-
11
2
-
4
-
27
5
26
6
9
7
8
0
9
41
53
8
0
1
-
1
2
0
2
-
1
-
6
-
2
-
3
0
1
3
-
14
-
12
2
-
1
-
7
-
5
-
1
DCT
Q
IQ

## Slide 15: An Example of JPEG Encoded Image
Original
JPEG Encoded

## Slide 16
H.261

## Slide 17: H.261
  Initial driving application: ISDN videoconferencing
  New technology used:
  MCPC(Motion compensated predictive coding)
ISDN(integrated service digital network)：整合電話電報等等轉類比成數位的系統
MCPC：只coding frame之間的差異(但是有delay，因為依賴前面的frame)

## Slide 18: H.261
JPEG + Motion Compensated Predictive Coding (MCPC)
reference frame
current frame
best matched block
Block-based coding，coding （mvx，mvy）（block移動了多少）+block residue（block內的差異）

## Slide 19
Encoder
Decoder
current
frame
previous
frame
residuals
MV
Motion Compensation Prediction (MCP)

## Slide 20: Motion Compensated Predictive Coding
Frame2 with MV
MC prediction error frame
Frame 1
Frame 2

## Slide 21: H.261 Video Codec
DCT
Q
VLC
IDCT
Motion
Compensated
Prediction
Buffer
-
IQ
Video
In
+
+
VLC: variable-length coding
decode時的ref. Frame是用reconstructed ref.，因為經過encode decode 後一定會有誤差，所以不是raw data

## Slide 22
MPEG-1

## Slide 23: MPEG-1
  Initial driving application: video CD
  New concepts:
  bi-directional motion estimation with half-pixel accuracy
Half-pixel為在pixel間再新增對半點，使移動可以為0.5（原為integer），可以讓轉的品質變好

## Slide 24: MPEG-1
Frame N-1
Frame N
Frame N+1
H.261 + half-pixel bi-directional MCPC

## Slide 25: Group of Pictures
I = Intra-picture coding, allow random access, for reference
P = Predictive coding, causal prediction only, can be referenced
B = Bi-directional coding, noncausal prediction, never referenced
品質來說I > P > B，v.s. H.261這個會誤差越來越大（因為計算ref一直下去），不像這個有一定時間就拿到I，可以不會一直錯下去

## Slide 26
MPEG-2

## Slide 27: MPEG-2
  Initial driving application: video-on-demand over HFC (hybrid fiber coaxial) networks
  Main new concepts:
  * Frame-field adaptive DCT and motion estimation
  * Profiles and levels
  * Scalable coding
  The most successful video standard for high quality applications (DVD, Digital TV, HDTV, ...)
  - Not suitable for low-bit-rate applications, due to the overheads
scalable coding就是在coding時縮小並計算縮小放大後（interpolation）與原圖的差異（residue），進行傳輸

## Slide 28: Profiles and Levels
Levels
Profiles
Simple
Main
SNR
Scalable
Spatially
Scalable
High
High
1920x1152
(60 frames/s)
High-1440
1440x1152
(60 frames/s)
Main
720x576
(30 frames/s)
Low
352x288
(30 frames/s)
10.4 Ms/s
15 Mbit/s
62.7 Ms/s
80 Mbit/s
47 Ms/s
60 Mbit/s
10.4 Ms/s
15 Mbit/s
3.04 Ms/s
4 Mbit/s
10.4 Ms/s
15 Mbit/s
for 2 layers
47 Ms/s
60 Mbit/s
for 3 layers
100 Mbit/s
for 3 layers
3.04 Ms/s
4 Mbit/s
for 2 layers
80 Mbit/s
for 3 layers
20 Mbit/s
for 3 layers
* numbers in the table are maximum allowed

## Slide 29: Frame/Field Adaptive Coding
16
16
16
8
Frame format
Field format

## Slide 30: H.263
  Initial driving application: videophone / wireless video
  New technologies: 4 optional modes
  Suitable for low-bit-rate applications due to the optimized overheads
  Current driving applications: internet / wireless video

## Slide 31: Four Negotiable Options
Annex D: unrestricted motion vector
Motion vectors can point outside the picture, maximum range for motion vectors: -31,5 to 31.5 instead of -16 to 15.5 (useful in case of higher resolution format and movement along the edge of the picture and camera movement)
Annex F: advanced prediction mode
8x8 motion vectors, overlapped block motion compensation (OBMC), motion vector can point outside the picture
Annex E: syntax-based arithmetic coding
About 5% decrease in bit-rate
Annex G: PB-frame mode
overlapped block motion，可以blocking effect reduction

## Slide 32: H.263+ / H.263 Version 2
Annex D: New Unrestricted Motion Vector Mode (use RVLC,
motion vector range up to +/- 256)
Annex I: Advanced Intra Coding Mode
Annex J: Deblocking Filter Mode
Annex L: Supplemental enhancement information specification
Annex M: Improved PB-Frame Mode
Annex O: Temporal, Spatial, and SNR Scalability Mode
Annex P: Reference Picture Resampling Mode
Annex Q: Reduced Resolution Update Mode
Annex S: Alternative Inter VLC Mode
Annex T: Modified Quantization Mode
Annex K: Slice Structured Mode
Annex R: Independent Segment Decoding Mode
Annex N: Reference Picture Selection Mode
Error resilience:
在variable-length coding中，若其中的bit變了，就會一直錯下去。解法：新增SYN（synchronization codeword），表示從這邊開始又是新的字，重新開始decode
RVLC（reversible variable-length coding），對其進行順向decode與從SYN 往前逆向decode，如果到某處兩邊都發生出錯，則此處即為錯誤點

## Slide 33
MPEG-4

## Slide 34: MPEG-4
  Initial driving application:
  1. Next generation video coding for very low bit-rate video
  2. Object based manipulation
    New concepts: object-based coding
  Driving application:
  MPEG-4 attempts to become the standard for streaming AV media on the Internet and via wireless networks
  Error-resilience features, optimized for low-bit-rate applications, fine granular scalability coding
  MPEG-4 file format defines first standard for streaming AV media on the Internet

## Slide 35: MPEG-4 Video Object Planes (VOP)
VOP1
VOP3
VOP2

## Slide 36: Synthetic and Natural Hybrid Coding (SNHC)

## Slide 37: MPEG-4 Texture and Shape Coding

## Slide 38
VOP-Based Encoding
VOP1
VOP2
VOP3
content-based
bitstream access
& manipulation
content-based
scalability
video objects
segmentation
& object mask
layered encoding
separate decoding
bitstream
(VOP3)
bitstream
(VOP2)
bitstream
(VOP1)

## Slide 39: MPEG-4 VOP Decoder
Shape
Decoding
Texture
Decoding
Shape Information
D
E
M
U
L
T
I
P
L
E
X
E
R
Motion
Compensation
Bitstream
Motion
Decoding
VOP
Memory
Reconstructed
VOP
Compositor
Video
output
Compositing script

## Slide 40: Sprite Coding
+

## Slide 41: MPEG-4 Visual Face Animation

## Slide 42: MPEG-4 ASP (Advanced Simple Profile)
previous techniques + ¼-pixel ME + Global ME
(
x’
3
,y’
3
)
(
x’
1
,y’
1
)
(
x’
2
,y’
2
)
(
x’
0
,y’
0
)
(
x
3
,y
3
)
(
x
2
,y
2
)
(
x
1
,y
1
)
(
x
0
,y
0
)
global motion estimation(ME)：Aflime transform(translation+rotation+scaling)

## Slide 43: MPEG-4 FGS (fine granularity scalability)
DCT
Q
Q-1
IDCT
Motion
Compensation
Motion
Estimation
Frame
Memory
VLC
Input Video
Base Layer
Bitstream
Shift
Bitplane
Find
Maximum
Bit-plane
VLC
Enhancement
Bitstream
FGS Enhancement Encoding
Clipping
MSB0 1000000000000000 …00
MSB1 0010000000000000 …00
MSB2 1010010110010000 …00
MSB3 0000010000000010 …00

## Slide 44
JPEG-2000

## Slide 45: The JPEG-2000 Architecture
JPEG-2000: discrete wavelet transform (DWT) + embedded block coding with optimum truncation (EBCOT)
EBCOT
Storage
or
Channel
Input
Output
DWT
Quantizor
Inverse
EBCOT
Inverse
DWT
Inverse
Quantizor
與jpeg的DCT(block-based)不同，透過整張進行low/high pass filter，因為大部分都是低頻，所以資訊都留在左上，越右下越沒東西。但是這樣計算下來jpeg所需的計算/memory較小，所以還是比較好用

## Slide 46: Quality Scalability with JPEG-2000
32:1
Compression Ratio
16:1
8:1
4:1
Improve decoding quality as receiving more bits

## Slide 47: JPEG-2000 vs. JPEG (1/3)
0.125bpp, JPEG
0.125bpp, JPEG-2000

## Slide 48: JPEG-2000 vs. JPEG (2/3)
0.25bpp, JPEG
0.25bpp, JPEG-2000

## Slide 49: JPEG-2000 vs. JPEG (3/3)
6 observers
6 color images
300 dpi
36%
53%
18%
11%

## Slide 50: MPEG-7: Multimedia Content Description Interface
To define standardized solutions that allow users or
agents to search, browse, filter audiovisual content.
User
Search Engine
Image Database
input
query
(MPEG-7)
visualization of result images
human
in the
loop
user feedback
user categories

## Slide 51: MPEG-7: Description of Multimedia Information
Text
How can “non-text-information” be described in a useful
way?
Speech- and Audio-Descriptors
        Pitch
        Melody
        Frequency
        Sex of speaker
Visual Clues
  Texture
  Color
  Form and Shape (2D/3D)
  Motion Activity
  Higher Order Object-Models
  Persons, Gestures

## Slide 52: What MPEG-7 Standardize?
Description Definition
Language (DDL)
Descriptors
Description Schemes
Flexible description
of description schemes
or descriptors
- XML Schema
Relations between
descriptors
- shape + motion
- shape + frame no
- Text,
- Color, Texture
- Shape, Motion
- Pitch, Melody

## Slide 53
MPEG-4 AVC/H.264

## Slide 54: MPEG-4 AVC/H.264: Features
Motion compensated DCT-like transform
I, P, B, SP, SI
Multiple reference frames
Variable block size – 7 block patterns: 16x16, 16x8, 8x16, 8x8, 8x4, 4x8, 4x4
Up to 16MVs per MB
4x4 integer DCT like transform
Improved intra prediction
Deblocking filter
Interlace coding tools
Universal VLC
Arithmetic coding (CABAC)
1/4 pel interpolation

## Slide 55: MPEG-4 AVC/H.264: Encoder Architecture
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal

## Slide 56: MPEG-4 AVC/H.264: Motion Compensation
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
Motion vector accuracy 1/4 (6-tap filter)
8x8
0
4x8
0
1
0
1
2
3
4x4
8x4
1
0
8x8
Types
0
16x16
0
1
8x16
MB
Types
8x8
0
1
2
3
16x8
1
0

## Slide 57: MPEG-4 AVC/H.264: Intra Prediction
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
Directional spatial prediction
(9 types for luma(亮度，對應Y), 1 chroma(顏色，對應Cb、Cr))
e.g., Mode 3: diagonal down/right prediction a, f, k, p are predicted by (A + 2Q + I + 2) >> 2
1
2
3
4
5
6
7
8
0
Q A B C D E F G H
I a b c d
J e f g h
K i j k l
L m n o p
M
N
O
P

## Slide 58: MPEG-4 AVC/H.264: Transform Coding
Entropy
Coding
Scaling & Inv. Transform
Motion-
Compensation
Control
Data
Quant. Transf. coeffs
Motion
Data
Intra/Inter
Coder
Control
Decoder
Motion
Estimation
Transform/ Scal./Quant.
-
Input
Video
Signal
Split into
Macroblocks
16x16 pixels
Intra-frame
Prediction
De-blocking
Filter
Output
Video
Signal
4x4 Block Integer Transform
Main Profile: adaptive block size transform (8x4,4x8,8x8)
Repeated transform of DC coeffs for 8x8 chroma and 16x16 Intra luma blocks

## Slide 59: MPEG-4 AVC/H.264: Multiple Reference Frames
Entropy
Coding
Motion
Data
Deq./Inv. Transform
Motion-
Compensated
Predictor
Control
Data
Quant. Transf. coeffs
0
Intra/Inter
Coder
Control
Decoder
Motion
Estimator
Transform/ Quantizer
-
Multiple Reference Frames for
Motion Compensation

## Slide 60: MPEG-4 AVC/H.264: Deblocking Filter
1) without filter 2) with H264/AVC deblocking
Deblocking filter: highly compressed decoded inter picture

## Slide 61: Coding Efficiency Comparison (1/4)
0
100
200
300
400
500
26
28
30
32
34
36
38
Foreman
10 Hz, QCIF
100 frames encoded
Integer-pel
motion
compensation
(H.261 1991)
Half-pel
motion
compensation
(MPEG-1 1993)
Frame
difference
coding
(H.120 1988)
Intraframe
DCT coding
(DCT 1974,
JPEG 1992)
PSNR
[dB]
bit-rate [kbps]
?
67 %
TMN-10
Variable
block size
motion
compensation
(H.263 1998)

## Slide 62: Coding Efficiency Comparison (2/4)
27
28
29
30
31
32
33
34
35
36
37
38
39
0
50
100
150
200
250
bit-rate [kbit/s]
Foreman QCIF 10Hz
Y-PSNR [dB]
MPEG-2
H.263
MPEG-4
JVT/H.264/AVC

## Slide 63: Coding Efficiency Comparison (3/4)
Alias 24 fps SDTV
25
30
35
40
45
50
0.00
0.50
1.00
1.50
2.00
2.50
3.00
3.50
4.00
4.50
5.00
Mbit/sec
Y PSNR [dB]
MPEG-2(QP 2-7)
AVC (QP 10,18,26)

## Slide 64: Coding Efficiency Comparison (4/4)
1st
MPEG-2 Encoder
2nd Generation Encoder
3rd Generation Encoder
4th Generation Encoder
H.264 /
MPEG-4 part 10
5th Generation Encoder
Source: Modulus Video

## Slide 65: How were the improvements obtained
- Better prediction
- More computation
- More memory
It mainly comes from incremental improvements:
No fundamental changes in the basic algorithm
(DCT + MCPC)

## Slide 66: What Else Besides Compression? (1/2)
Networking (wired and wireless):
Scalable coding, Multiple description coding,
Transcoding, Statistical multiplexing, Error-
resilience coding, Error-concealment, Pre/post
processing, Dynamic rate-control, Content-aware
delivery, Joint source channel coding, Peer-to-
peer streaming, Wireless games, …

## Slide 67: What Else Besides Compression? (2/2)
Asynchronous applications may see more early success: needs authoring, retrieval, and content filtering tools
Security: advanced video surveillance, face recognition, …
Content protection: IP Protection, encryption, watermarking, …
Implementation: for low-cost low-power high-performance devices, media processors