## Slide 1
Chapter 6.
Other Compression Techniques
Vector quantization (VQ)
Fractal coding
Subband and wavelet coding
Model-based coding

## Slide 2: Vector Quantization

## Slide 3: Vector Quantization (Cont.)
Codebook
...
...
...
...
Best Match
Search
Table
Lookup
index

## Slide 4: LBG Algorithm
Linde, Buzo, Gray (1980): Lloyd algorithm generalized for VQ
Assumption: fixed codeword length
Code book unstructured: full search
Best representative
vectors
for given subdivision
of training set
Best subdivision
of training set
for given
representative vectors

## Slide 5: VLC VQ
Chou, Lookabaugh, Gray (1989): extended LBG algorithm for entropy-coded VQ
Lagrangian cost function to solve an unconstrained problem:
  min{D+R}
Unstructured codebook: full search for min{D+R}
The most general coder structure:
any source coder can be interpreted as VQ with VLC

## Slide 6: Lattice Vector Quantization

## Slide 7: 8D VQ of Gauss-Markov Source
Shannon lower bound

## Slide 8: Vector Quantization
Highly asymmetrical encoding and decoding complexity
Encoding complexity depends on the codebook size
Decoding is done simply by table lookup
Codebook design usually is an iterative process, which
involves off-line training
Different codebook designs result in different quality

## Slide 9: Fractals

## Slide 10: Affine Transformation
]
x’
y’
[
]
a b
c d
[
]
x
y
[
]
e
f
[
=
+
Maps points into new points according to affine transform:
Can model translation, rotation, and scaling.

## Slide 11: Fractal Image Coding
Partition the image
into DOMAIN regions
Choose a set of allowable
RANGE regions
Point to the first DOMAIN
Find the affine transform
and the best matched RANGE
Store the affine coefficients
Last
DOMAIN ?
Output header and the
packed affine coefficients
Choose the class of
affine transforms
Point to next
DOMAIN
N
Y

## Slide 12: Fractal Image Decoding
Read domain partition info
and unpack affine coef.
Create memory buffers for the
DOMAIN and RANGE screens
Point to the first DOMAIN
Replace DOMAIN with transformed
data using the affine coefficients
Store the affine coefficients
Last
DOMAIN ?
Copy contents of DOMAIN
screen to RANGE screen
Initialize the RANGE
screen buffer to an
arbitrary initial state
Point to next
DOMAIN
N
Y
More
iterations?
Y
Output the
final DOMAIN
screen
N

## Slide 13: Fractal Coding
- Real-time encoding is a problem
- Currently quality may not be better than JPEG and MPEG
(especially for high quality applications)
- Real-time decoding can be implemented using regular PC
- Resolution independent

## Slide 14: Interpolation Error Coding

## Slide 15: Interpolation Error Coding (Cont.)
Signals to be encoded

## Slide 16: Predictive Pyramid Coding

## Slide 17: Predictive Pyramid Coding (Cont.)
subsampling factor

## Slide 18: Predictive Pyramid Coding (Cont.)
Signals to be encoded

## Slide 19: Interpolation Error Coding vs. Pyramid
Interpolation error coding
Pyramid
Resolution layer #0, interpolated to original size for display

## Slide 20: Interpolation Error Coding vs. Pyramid (Cont.)
Interpolation error coding
Pyramid
Resolution layer #1, interpolated to original size for display

## Slide 21: Interpolation Error Coding vs. Pyramid (Cont.)
Interpolation error coding
Pyramid
Resolution layer #2, interpolated to original size for display

## Slide 22: Interpolation Error Coding vs. Pyramid (Cont.)
Interpolation error coding
Pyramid
Resolution layer #3
=
(original)

## Slide 23: Open-loop Pyramid (Laplacian Pyramid)

## Slide 24: Two-layer Open- vs. Closed-loop Pyramids

## Slide 25: Subband Coding

## Slide 26: Two-Band Analysis Filter Band
To eliminate aliasing distortion, the synthesis and analysis filters must have certain relationships
frequency
amplitude
W/2
low band
high band
W
0

## Slide 27: Two-Band Subband Codec
2
2
S
X(z)
Y(z)
H
0
(
z
)
H
1
(
z
)
G
1
(
z
)
G
0
(
z
)
2
2
downsample by a factor of 2
upsample
coding and
transmission
the z-transform of the low-pass analysis filter
the z-transform of high-pass analysis filter
and are the corresponding synthesis filters
The downsampling factor is 2, so as the upsampling

## Slide 28: Perfect Reconstruction in Subband Coding
The reconstructed output in z-transform notation:
where
The aliasing components from the downsampling of the lower and higher bands are given by H0(-z)X(-z) and H1(-z)X(-z), respectively. Then

## Slide 29: Perfect Reconstruction in Subband Coding
The first term is the desired reconstructed signal, while the second term is aliased components. That is
With such a relation between the synthesis and analysis filters, the reconstructed signal now becomes:

## Slide 30: Example: Two-channel Filter Bank with Perfect Reconstruction

## Slide 31: Quadrature Mirror Filter

## Slide 32: Subband and Wavelet Coding
8f0
4f0
2f0
f0
16f0
0
frequency
amplitude
0
frequency
amplitude
5f0
3f0
2f0
f0
10f0
4f0
6f0
7f0
8f0
9f0
Subband Decomposition
Wavelet Decomposition

## Slide 33: Subband and Wavelet Coding (Cont.)
h(n)
g(n)
2
2
2
2
h’(n)
g’(n)
h(n)
g(n)
2
2
h(n)
g(n)
2
h(n)
g(n)
2
2
2
+

## Slide 34: 2-D Discrete Wavelet Transform (Cont.)

## Slide 35: Similarities among Image Subbands

## Slide 36: Zerotree Coding of Higher Bands
The higher order wavelet coefficients are coded with the embedded zero-tree wavelet (EZW)
  based on the concept of quantization by successive approximation,
  exploits the similarities of the bands of the same orientation.

## Slide 37: Principle of Successive Approximation
  The quantized length can be expressed as
L
l
l/2
l/8
l/4
l/16
l/32

## Slide 38: Zerotree Coding: Quadtree Representation of Higher Bands
Subimages of lower bands have quarter dimensions of their higher bands
A quad-tree representation of the bands of the same orientation for a 10-band splitting is shown below
If a coefficient in LH3 is zero, it’s more likely that its children in higher bands of LH2 and LH1 will also be zero => “zero tree”
HL1
LH1
HH1
LL
LH2
LH3
HH2
HH3
HL3
HL2

## Slide 39: Embedded Zerotree Wavelet Algorithm
Ideal:

## Slide 40: Embedded Zerotree Wavelet Algorithm (Cont.)
For the highest bands, ZTR and IZ symbols are merged into one symbol Z
Successive approximation quantization and encoding
  Initial “dominant” pass
    Set initial threshold T, determine significant coefficients
    Arithmetic coding of symbols ZTR, IZ, POS, NEG
  Subordinate pass
    Refine magnitude of coefficients found significant so far by one bit (subdivide magnitude bin by two)
    Arithmetic coding of sequence of zeros and ones.
  Repeat dominant pass
    Set previously found significant coefficients to zero
    Decrease threshold by factor of 2, determine new significant coefficients
    Arithmetic coding of symbols ZTR, IZ, POS, NEG
  Repeat subordinate and dominate passes, until bit budget is exhausted.

## Slide 41: A Coding Example of EZW
63 | -34 | 49 | 10 | 7 | 13 | -12 | 7
-31 | 23 | 14 | -13 | 3 | 4 | 6 | -1
15 | 14 | 3 | -12 | 5 | -7 | 3 | 9
-9 | -7 | -14 | 8 | 4 | -2 | 3 | 2
-5 | 9 | -1 | 47 | 4 | 6 | -2 | 2
3 | 0 | -3 | 2 | 3 | -2 | 0 | 4
2 | -3 | 6 | -4 | 3 | 6 | 3 | 6
5 | 11 | 5 | -6 | 0 | 3 | -4 | 4

## Slide 42: A Coding Example of EZW (Cont.)
Subband | Coef Value | Symbol | Rec Value
LL3 | 63 | POS | 48
HL3 | -34 | NEG | -48
LH3 | -31 | IZ | 0
HH3 | 23 | ZTR | 0
HL2 | 49 | POS | 48
HL2 | 10 | ZTR | 0
HL2 | 14 | ZTR | 0
HL2 | -13 | ZTR | 0
LH2 | 15 | ZTR | 0
LH2 | 14 | IZ | 0
LH2 | -9 | ZTR | 0
LH2 | -7 | ZTR | 0
HL1 | 7 | Z | 0
HL1 | 13 | Z | 0
HL1 | 3 | Z | 0
HL1 | 4 | Z | 0
LH1 | -1 | Z | 0
LH1 | 47 | POS | 48
LH1 | -3 | Z | 0
LH1 | -2 | Z | 0

## Slide 43: Features of The EZW Algorithm
The use of zero trees reduces the number of symbols to be encoded
The use of a very small alphabet to represent an image makes adaptive arithmetic coding very efficient
The maximum distortion of each pass is bounded by the threshold used in the pass
At any given pass, only the coefficients with magnitudes larger than the current threshold are encoded nonzero => prioritize the coefficients of different importance
With the successive approximation process, the encoding and decoding process can stop at any point
Embedded spatial/SNR scalability

## Slide 44: Embedded Zerotree Wavelet Algorithm (Cont.)
Decoding: bitstream can be truncated to yield a coarser approximation: “embedded” representation
JPEG-2000 standard similar to SPIHT

## Slide 45: Model-based Coding
Has potential to achieve very low bitrates by using
source models at both the encoder and decoder
- Object oriented coding
- Wired frame model

## Slide 46: Parameters of Object Based Coding
Shape
Motion
Texture
Information
.

## Slide 47: Wire-Frame Model