## Slide 1
Chapter 7. High Efficiency Video Coding (H.265)

## Slide 2: Outline
Video coding standards
Coding performance and complexity of HEVC
HEVC tool features
Other video coding extensions

## Slide 3: HEVC Goals
Simplicity and “back to basics” approach
Coding efficiency (e.g., 2*H.264 efficiency)
Computational efficiency
Loss/error robustness
Network friendliness
Other considerations

## Slide 4: High-Efficiency Video Coding

## Slide 5: Coding Performance
Max 43.7%
HM 2.0 vs.
JM17.0
- BD-rate: Bjøntegaard delta bit rate
- HE: high efficiency (10-bit codec), LC: low complexity
s
Y BD-rate savings (%)

## Slide 6: Time Complexity
HM 2.0 vs.
JM17.0
Dec Time < 74%
r
Time ratio

## Slide 7: Subjective Assessment
Bit rate [Kbps]

## Slide 8: Objective Measurement
Chart: HM7.0 vs. JM18.3
| Low Delay | Random Access | ALL Intra
BD | 0.367 | 0.337 | 0.221

## Slide 9: Objective Measurement
Class | Resolution | All Intra | Radom Access | Low Delay
 |  | Y BD-Rate | Y BD-Rate | Y BD-Rate
A | 2500x1600 | -23.7 | -36.7 | 
B | 1080p | -22.8 | -39.7 | -42.1
C | 480p | -19.9 | -30.0 | -32.3
D | 240p | -16.7 | -27.2 | -29.1
E | 720p | -29.1 |  | -43.7
F | 480p, 720p | -22.8 | -25.6 | -28.8

## Slide 10: Time Complexity
Chart: HM7.0 vs. JM 18.3
| Low Dwlay | Random Access | All Intra
Encding | 0.62 | 0.4 | 1.15
Decoding | 0.71 | 1.07 | 0.86

## Slide 11: HEVC Tool Features
Coding Unit (CU)
Prediction Unit (PU)
Current frame
Frame
buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
output bitstream
Transform Unit (TU)

## Slide 12: Coding Unit (CU)
MB
MB
Basic unit for coding, conceptually similar to macroblock, but now can be of variable-sized
CU
CU
CU
CU
CU
CU
CU
CU
64
64
CTU0
CTU1
HEVC
…
MB
16
16
H.264/AVC
…

## Slide 13: Prediction Unit (PU)
MB
CU
Sub-MB Partition
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
PU
(Only for SCU)
Asymmetric

## Slide 14: Transform Unit (TU)
Residual quad-tree transform (RQT)
Transform can cross PU boundaries
MB
TU
TU
TU
TU
TU
TU
TU
TU
TU
TU
TU
8
8
4
4
PU Aligned
CU
TU
TU
TU
TU
TU
TU
TU
TU
TU
TU
TU
TU
May be skipped
if 4 ×4
RQT

## Slide 15: HEVC Tool Features
Current Frame
Frame
Buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
output
bitstream
More Directions
Pre-/Post-filtering
Direct Chroma

## Slide 16: Intra Prediction
More directions (up to 33) + DC + planar
Adaptive pre-filtering of reference pixels
Boundary smoothing for DC/Ver./Hor. modes
Direct mode for chroma

## Slide 17: HEVC Tool Features
Current Frame
Frame
Buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
output bitstream
Asymmetric Motion Partitioning
Merged Skip, Motion Merging
Advanced MV Prediction
DCT-based Interpolation Filter

## Slide 18: Advanced Motion Vector Prediction

## Slide 19: Motion Merging

## Slide 20: Motion Merging

## Slide 21: DCT-based Interpolation Filter
  Interpolation by inverse DCT (DCT-IF)
{P-5, P-4, …, P6}
Spatial domain samples
{C-5, C-4, …, C6}
DCT domain coefficients
DCT
IDCT
Coefficients of DCT(P1~P2M-1)
Any sub-pel position
Inv-DCT

## Slide 22: HEVC Tool Features
Current Frame
Frame
Buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
bitstream
Residual Quad-tree Transform
Transform Skipping
Adaptive Coefficient Scanning

## Slide 23: Transform and Coefficient Scanning
Extended DCT size (up to 64x64)
Adaptive coefficient scanning
  Zigzag, horizontal, or vertical (Intra HE only)
  Zigzag (other settings)
Zigzag
Horizontal
Vertical

## Slide 24: HEVC Tool Features
Current Frame
Frame
Buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
output bitstream
Adaptive Loop Filter
Sample Adaptive Offset

## Slide 25: Adaptive Loop Filter
5×5 filter
CU Quad-tree
Depth=3
Segmentation Map
Depth=2
On
On
On
On
On
On
On
On
On
On
merge

## Slide 26: Sample Adaptive Offset
Sample-adaptive DC compensation
Band Offset (BO): intensity-based sample classification
Edge Offset (EO): edge-based sample classification

## Slide 27: Edge Offset (EO)
(a) positive edge offset
(b) negative edge offset

## Slide 28: HEVC Tool Features
Current Frame
Frame
Buffer
Intra Prediction
Inter Prediction
Entropy Coding
IQ
IDCT
DCT
Q
Inter
Intra
-
+
In-loop filter
+
+
bitstream
Modified CABAC
Tiles/Wavefront

## Slide 29: Low Complexity Entropy Coding
Context-adaptive table switch (same as CAVLC)
Adaptive mapping between event and codeword

## Slide 30: Arithmetic Precision Increase
Reduce rounding errors by
  Internal bit-depth increase (IBDI)
  Transform precision extension (TPE)
Increase word length
Decrease word length

## Slide 31: Slice and Tiles
Typical examples of (a) slice and (b) tile partitioning of a picture
Slice and tile partitioning are only allowed at the granularity of CTUs (CU level partitioning was possible but complicated)
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
CTU
Slice 1
…
…
Slice 2
…
…
…
…
Slice N
…
…
…
…
Tile 1
Tile N
(a)
(b)

## Slide 32: Wavefront Parallel Processing (WPP)

## Slide 33: HE10 vs. Main
Tools | High Efficiency (10-bit Codec) | Main Profile (8-bit Codec)
CU Size | 8x8~64x64 | 16x16~64x64
PU Partition | Symmetric/Asymmetric | 
TU Partition | RQT | 
MV Prediction | AMVP, MRG, MRG-Skip | 
Intra Prediction | DC, Planar, 33 Directions, DM | 
Transform | DCT 4x4~32x32, DST/Skip 4x4 (Intra) | 
Interpolation Filter | DCT-IF | 
In-loop Filter | De-blocking, SAO | 
Entropy Coding | CABAC (Tiles, WPP) | 
* Only Main Profile is adopted in the draft

## Slide 34: HEVC Scalable Extension
Goal: adding scalability to HEVC
  Spatial scalability
  Intra-only spatial scalability
  SNR scalability
  Coding standard spatial scalability (AVC BL)

## Slide 35: CfP Test Conditions
7 Sequences, 4 BL & 4 EL Rate Points
 | EL Resolution | BL Resolution |  | # of Seqs
 |  | 1.5x | 2x | 
Class A+ | 3840x2048 |  | 1920x1024 | 1
 | 3840x2160 |  | 1920x1080 | 1
Class B | 1920x1080 | 1280x720 | 960x540 | 5

## Slide 36: 3D Video Coding

## Slide 37: 3D Video Coding Progress
Totally 20 ad hoc group meeting on
  Free-viewpoint TV (in the past)
  3D video coding (in the past)
Standardization Tracks Considered in 3D Video Coding
  MVC compatible extension including depth
  AVC compatible video-plus-depth extension
  HEVC 3D extensions

## Slide 38: 3DV Experimental Framework
Advanced stereoscopic processing
Auto-stereoscopic display

## Slide 39: Standardization Tracks Considered in 3D Video Coding
MVC compatible extension including depth
AVC compatible video-plus-depth extension
HEVC 3D extensions